## Slide 1: Assessment of the use of a selection of natural deep eutectic solvents in the extraction of polar bioactive compounds from orange peel
Authors: Tejero-Martínez, A., Martín, M.E., Malo-López, D., Frígola, A., Esteve, M.J., Blesa, J

## Slide 2: WHAT ARE “NADES”?
NADES
DES
Eutectics Mixtures
Two compounds (solids)→ lowest melting point = Liquid phase at Eutectic temperature
1º INTRODUCTION
2 green solvent study sites: ILs and DES
Raw Materials
Easy Preparation
Biodegradability
Ideal ‘’Green’’ Solvents
Better extraction PF
Co-solvents
Less Viscosity
High mass transference
Hydrophilic Character
CONTEXT: Concern for the environment

## Slide 3
2º OBJECTIVES
Select 5 NADES, which showed the best results in their source articles as extractants of bioactive compounds on different plant residues, reversing the proportions of water and original NADES.
Perform an extraction on orange peel of bioactive compound, characterized as total phenols and antioxidant capacity, with the selection of NADES and compare them with a conventional extraction (Ethanol-Water 50%, v:v).
Check for changes in the stability of the 6 types of extracts over 4 weeks at a storage temperature of 4°C.

## Slide 4: PREPARATION OF SAMPLES AND EXTRACTS
3º MATERIALS AND METHODS
Weigh the orange and separate the peel
Grind the peel and weigh 7g
Weigh NADES components according to molar ratios
Heating Plate (50-90ºC)
Dilute with water (70%, v:v)
Solid-Liquid Ratio (1:10)
Centrifugation: 3000 rpm 10 min
Separating supernatant and skin
Conservation 4ºC
TOTAL: 36 samples
Extraction (20 min) with magnet stirring

## Slide 5: NADES SELECTED
Citric Acid-Glucose 1:1
Glucose-Glycerol
3:1
Choline-Citric Acid
2:1
Choline-Glycerol
3:1
Choline-Glucose
2:1
A conventional extractant is used as a reference: Ethanol-Water (50%)
The best-performing NADES were selected on the basis of different studies
Solid-Liquid Ratio 1:10
Extraction time: 20 min
All NADES 70%
3º MATERIALS AND METHODS

## Slide 6: TOTAL PHENOLIC COMPOUNDS (TPC)
4º RESULTS
2 Groups: The lowest values ​​are showed by the choline combinations
Chart: PHENOLIC COMPOUNDS (mg/100g DW)
| Day 1 | Day 2 | Day 3 | Day 8 | Day 10 | Day 15 | Day 17 | Day 22 | Day 24
Citric Acid-Glucose | 5060 | 5090 | 5180 | 5060 | 4800 | 4620 | 4340 | 4410 | 4420
Ethanol-Water | 4680 | 4470 | 4320 | 3700 | 3820 | 4010 | 3760 | 3900 | 3730
Glucose-Glycerol | 4050 | 3930 | 4670 | 3970 | 4010 | 3620 | 3480 | 3220 | 3390
Choline Chloride-Citric Acid | 1380 | 1230 | 1310 | 1500 | 1540 | 800 | 1020 | 1180 | 1220
Choline Chloride-Glucose | 950 | 1000 | 1220 | 920 | 1180 | 880 | 830 | 810 | 810
Choline Chloride-Glycerol | 740 | 840 | 790 | 820 | 1060 | 740 | 590 | 650 | 700

## Slide 7: TOTAL ANTIOXIDANT CAPACITY (TAC)
Better results: Glycerol combinations
4º RESULTS
Chart: Inhibition (%) DPPH
| Day 1 | Day 2 | Day 3 | Day 8 | Day 10 | Day 15 | Day 17 | Day 22 | Day 24
Choline Chloride-Glycerol | 41.6767 | 46.955 | 52.0342 | 46.5737 | 48.2437 | 45.1066 | 48.7231 | 38.7103 | 36.6165
Glucose-Glycerol | 40.1135 | 43.9664 | 41.8517 | 39.0609 | 44.4191 | 36.2933 | 45.8444 | 36.5464 | 32.0626
Choline Chloride-Glucose | 36.472 | 41.9242 | 46.8695 | 37.055 | 39.392 | 38.4986 | 33.3292 | 33.3457 | 29.8772
Choline Chloride-Citric Acid | 36.435 | 43.3431 | 44.1342 | 34.8113 | 40.8746 | 35.557 | 41.6782 | 34.2219 | 35.9
Ethanol-Water | 32.9372 | 27.2121 | 32.615 | 24.9878 | 26.1904 | 24.747 | 28.0073 | 17.4002 | 14.8299
Citric Acid-Glucose | 26.9323 | 27.7272 | 24.7484 | 26.9793 | 29.2047 | 22.2281 | 14.8299 | 21.5471 | 21.9769

## Slide 8: STABILITY TEST
4º RESULTS
Significant differences from day 15
Reduction in all of them

## Slide 9
5º DISCUSSION
Comparation with some studies
Mouratoglou et al. (2016)
NADES 10%
Panić et al. (2021):
ChCl-Gly 50% ; Glu-Gly 80%
Ahmad et al. (2018)
NADES 50%
TAC
69 (lemon) y 96% (orange) DPPH reduction
59% DPPH reduction
Kolarević et al. (2020)
NADES 20%
Jeong et al. (2015)
NADES 70%
MÁX. 52% DPPH reduction
Best extraction by NADES (AC-Glu) 5180 mg GA / 100 g DW.
And 4680 mg AG / 100 g DW for the Ethanol-Water.
Better results of the NADES with hydrophilic character.
TPC
REFERENCE SOLVENT
NOT COMPARED
5370 mg GAE/100 g DW
5100 y 5200 mg GAE/100 g FW
2710 mg GAE/100 g DW (ethanol)
4000 mg GAE/100 g FW (ethanol)
8701 y 6291 mg GAE/100 g DW

## Slide 10: Comparation with some studies: STABILITY
5º DISCUSSION
This may indicate that Ethanol-Water extract has obtained other antioxidant compounds apart from polyphenols such as vitamin C and therefore there has been this difference in final TAC.
TPC
Retention of studies: 99-93% (Max.) And 85-66% (Min.)
TAC
Retention of studies: 99-97% (Max.) And 82-70% (Min.)
There have been significant reductions in all of them from day 15 at 4ºC. In the studies they were between 2-6 months.
The retention in this work: 94.6-83.7% in NADES and 79.7% (Ethanol-Water)
The retention in this work: 98.3-77.5% in NADES and 43.5% (Ethanol-Water)
There has been a correlation between the reduction of PFT and CAT in the NADES. Except Ethanol-Water.
Not compared with NADES!

## Slide 11
6º CONCLUSIONS
The highest TPC extraction was obtained by NADES AC-Glu with 5180 mg GAE / 100g DW with significant differences compared to the rest and the Ethanol-Water extract (50%, v: v) with 4680 mg GAE / 100g weight dried.
2. The highest TAC was obtained by the NADES whose combinations presented Gly (ChCl-Gly and Glu-Gly) with up to 52 and 45.8% reduction in DPPH but Ethanol-Water (50%, v: v) that achieved 29.2% reduction.
3. The retention of TPC in 4 weeks of analysis has been between 94.6 and 83.7% in the NADES while that of the Ethanol-Water (50%, v: v) decreased to 79.7%.
4. TAC retention in 4 weeks of analysis has been between 98.3 and 77.5% in the NADES while that of Ethanol-Water (50%, v: v) was the lowest with 43.5%.
5. It has been found that a higher proportion of water in NADES has led to better TPF and TAC extractions than most studies using smaller amounts.
6. The stability of TPC and TAC has been maintained until day 15 of analysis, showing correlation in the reduction of TPC with TAC except for the Ethanol-Water extract where other antioxidants have been able to intervene.