## Slide 1
Treatment of winery wastewater by an EDDS-photo-Fenton process. Assessment of UV-C, UV-A and solar radiation
The 1st International Electronic Conference on Processes: Processes System Innovation
Session 2. Environmental and Green Processes
17 – 31 May 2022
Nuno Jorge1,2 *; Carlos Amor2; Ana R. Teixeira2; Leonilde Marchão2; Marco S. Lucas2; José A. Peres2
1 Escuela Internacional de Doctorado (EIDO), Campus da Auga, Campus Universitário de Ourense, Universidade de Vigo, As Lagoas, 32004, Ourense, Spain
2 Centro de Química de Vila Real (CQVR), Departamento de Química, Universidade de Trás-os-Montes e Alto Douro (UTAD), Quinta de Prados, 5001-801,
Vila Real, Portugal
* njorge@uvigo.es

## Slide 2
Introduction
Winery wastewater main characteristics
Winery wastewater
Soluble sugars
pH
Alcohols
Organic acids
BOD5
High-molecular-weight compounds
COD
Fructose
Glucose
Tartaric acid
Lactic acid
Acetic acid
Glycerol
Ethanol
3 - 4
125 – 130 000 mg O2 L−1
320 – 296 000 mg O2 L−1
Polyphenols
Tannins
Lignin
Mass balance applied to ACPB winery representing specific values, i.e., values per cubic meter of produced wine. Losses of water by evaporation were neglected [1].
[1] Brito, A. G., Peixoto, J., Oliveira, J. M., Oliveira, J. A., Costa, C., Nogueira, R., & Rodrigues, A. (2007). Brewery and winery wastewater treatment: some focal points of design and operation. In Utilization of by-products and treatment of waste in the food industry (pp. 109-131). Springer, Boston, MA.

## Slide 3
Photo-Fenton process
Catalyst
Oxidant
Radiation
UV-C Mercury lamp
UV-A LED lamps
Solar light
Iron
Copper
Cobalt
Magnesium
Manganesium
Zinc
Hydrogen peroxide (H2O2)
Introduction
Chelating agents
Oxalate
EDDS
EDTA
NTA

## Slide 4
Objectives
(1) Study the impact of EDDS on Fe2+ regeneration in photo-Fenton process
(2) Study the effects of EDDS and HA on hydroxyl radical production in photo-Fenton process
(3) Study the impact of radiation type in organic matter removal
The aim of this work is

## Slide 5
Material and methods
Parameters | Portuguese Law Decree nº 236/98 | WW
pH | 6.0-9.0 | 4.0
Biochemical Oxygen Demand - BOD5 (mg O2/L) | 40 | 550
Chemical Oxygen Demand - COD (mg O2/L) | 150 | 2145
Biodegradability – BOD5/COD |  | 0.26
Total Organic Carbon – TOC (mg C/L) |  | 400
Turbidity (NTU) |  | 296
Total suspended solids – TSS (mg/L) | 60 | 750
Electrical conductivity (μS/cm) |  | 62.5
Total polyphenols (mg gallic acid/L) | 0.5 | 22.6
Iron (mg/L) | 2.0 | 0.05
Aluminium (mg/L) | 10.0 | 
Cobalt (mg/L) |  | 0.00
Manganese (mg/L) | 2.0 | 
Potassium (mg/L) |  | 20.5
Calcium (mg/L) |  | 1.07
Magnesium (mg/L) |  | 0.51
Sodium (mg/L) |  | 0.19
Winery wastewater characterization
Main chemical characteristics of winery wastewater (WW)
Winery wastewater collection and storage
Winery wastewater used in this work
Storage in small containers
Conservation at -40ºC

## Slide 6
Equipment used in photo-Fenton process
UV-A LED
reactor
UV-C mercury lamp
reactor
Magnetic agitators
Solar reactor
Silver
coated
panel
UV absorption spectra corresponding to WW and WW+Fe2++EDDS+HA.
Material and methods

## Slide 7
Results and discussion
(1) Variation of [H2O2]
(3) Variation of catalyst type
(5) Variation of the HA dosage
(2) Variation of [Fe2+]
(4) Variation of the EDDS dosage
(6) Variation of radiation type vs pH
Evolution of COD removal through the photo-Fenton experiments, using different catalyst dosages
93.4%
88.0%
82.5%
68.4%
Fe2+ + H2O2 → Fe3+ + + | Eq. 3
Fe3+ + H2O2 → Fe2+ + + H+ | Eq. 4
 | Eq. 3
 | Eq. 4
+ H2O2 → H2O + | Eq. 1
+ → H2O + O2 | Eq. 2
 | Eq. 1
 | Eq. 2
Influence of different sulfate salts in the removal of COD.
Effect of catalyst concentration
Effect of catalyst type

## Slide 8
Results and discussion
(1) Variation of [H2O2]
(3) Variation of catalyst type
(5) Variation of the HA dosage
(2) Variation of [Fe2+]
(4) Variation of the EDDS dosage
(6) Variation of radiation type vs pH
86.2%
89.8%
92.6%
99.5%
94.8%
Evolution of COD removal through the photo-Fenton experiments, using different HA concentration.
Effect of hydroxylamine concentration
Effect of radiation type
Evolution of the (a) COD removal, (b) ORP value through the photo-Fenton experiments, under the influence of different UV sources at pH 3.0 and 6.0.

## Slide 9
Conclusion
Based in the results it is concluded
1. The application of 175 mM H2O2 achieves a high COD removal (82.5%), high HO• radical production (240.3 mV) and low metal leaching (1.79 mg Fe/L)
2. The type of catalyst has a great influence in the organic matter removal, and that the Fe2+ is concluded to be the most efficient catalyst
3. The radicals generation are greatly promoted with the addition of hydroxylamine and the molar ratio of EDDS-Fe/HA system (1/5/1) achieves higher COD removal (99.4%)
4. With application of the Fe2+-EDDS/HA system it is concluded that the photo-Fenton process at pH 6.0 achieves similar COD reductions regarding pH 3.0.
5. The solar radiation achieves similar COD removal than UV-A radiation and is concluded to be a viable alternative.

## Slide 10
Acknowledgements
The authors thank the North Regional Operational Program (NORTE 2020) and the European Regional Development Fund (ERDF), and express their appreciation for the financial support of the Project AgriFood XXI, operation nº NORTE-01-0145-FEDER-000041, and to the Fundação para a Ciência e a Tecnologia (FCT) for the financial support provided to CQVR through UIDB/00616/2020. Ana R. Teixeira also thanks the FCT for the financial support provided through the Bolsa de Doutoramento UI/BD/150847/2020.

## Slide 11
Thank you for your attention