## Slide 1
Wear amount measuring method using red lead paint
to innovate sensory inspection for female taper socket
of machine tools
Kaito FUJIYOSHI1, Mikihiko MAWATARI1, Ichiro YOSHIDA2
HOSEI University, Graduate School of Science and Engineering, Major in Mechanical Engineering
HOSEI University, Faculty of Science and Engineering, Department of Mechanical Engineering
Correspondence: Ichiro Yoshida, HOSEI University, E-mail: yoshida.ichiro@hosei.ac.jp
Background
Purpose
Method
Conclusion
Taper shank and tool
Female taper socket
Cross-sectional view of female taper
In the future, IoT and full automation will be essential.
Painted ring gauge.
Photograph of
imaging device.
photographed image with infrared camera.
Luminance values.
As regards the maintenance for female tapers of machine tools, sensory inspection has been standardized in both JIS and ISO standards. Therefore, highly skilled operators are required.
In order to promote automation and improve productivity by IoT, human workload needs to be reduced.
・Develop new measurement method that is less dependent on an operator's skill level.
・Achieve quantification, skillless and automation maintenance.
Ring gauge is used instead of the female taper .
The paint is applied onto the measurement surface.
The amount of wear is calculated.
The most suitable concentration of red lead paint for measuring
the amount of wear is that when ratio of red lead powder to oil is 1:1.
Decide the concentration of red lead paint necessary for accurately measuring the amount of wear.