## Slide 1
Holography with incoherent light
Akanksha Gautam,1,* Athira T S,2 Dinesh N. Naik,2 C. S. Narayanamurthy ,2 Rajeev Singh,1
Rakesh Kumar Singh1
1Laboratory of Information Photonics and Optical Metrology, Department of Physics, Indian Institute of Technology (Banaras Hindu University), Varanasi-221005, India
2Applied and Adaptive Optics Laboratory, Department of Physics, Indian Institute of Space Science and Technology, Thiruvananthapuram-695547, India
We present a possible experimental approach for holography with the incoherent light. In case of incoherent light, the complex spatial coherence function is a measurable quantity and the incoherent object holograms are recorded as the coherence function. Thus, to record the complex spatial coherence a square Sagnac radial shearing interferometer is designed with the phase-shifting approach. The five-step phase-shifting method helps to measure the fringe visibility and the corresponding phase, which jointly represents the complex coherence function. The inverse Fourier transform of complex coherence function helps to retrieve the object information.
Digital holography (DH) is a technique of interference of two waves. The recorded interference pattern contains both amplitude and phase information which can be further reconstructed on digitally processing of the recorded hologram.
A coherent source is utilized to achieve the interference in the DH, but the coherent imaging system suffers from speckle noise and edge effects.
Whereas, the incoherent imaging systems are free from speckle noise.
The interference of incoherent light reflected or emitted from an object result in incoherent digital holograms.
Many known methods of recording incoherent holograms are based on the self-interference principle, and it can generate an interference pattern with light coming from its mirror imaged point.
These techniques record the incoherent hologram in the form of intensity patterns. The other way to record an incoherent hologram is in the form of two-point spatial complex coherence function .
In this paper, we present an experimental approach to record an incoherent object hologram as the spatial coherence function.
The field is Fourier transformed using a lens L having a focal length f and at Fourier plane, a single realization of the field is represented as
Figure 1. Geometry for recording information of spatial coherence function
f
f
E(r1)
E(r2)
Г(r1, r2)
L
η(r; λ)
˜
, ) =
, ) =
P2
QWP
L1
L3
L2
L4
M3
M2
M4
PBS
Camera
L3
M3
M2
M1
f1
f1
f2
f3
f2+f3
P1
LED Source
The integral inside the curly bracket represents van Cittert-Zernike theorem.
Figure 2. Experimental set up square Sagnac radial shearing interferometer: P: Polarizer, L: Lens, BS: Beam Splitter, M: Mirror, QWP: Quarter Wave Plate
Figure 3. Digitally constructed coherence function (a)fringe visibility (b) corresponding phase and (c) reconstructed object intensity distribution
Now, to reconstruct the object intensity distribution the spatial coherence function is inverse Fourier transformed
We have presented an experimental method using shearing for holography with the incoherent source. The object information is recorded in the form of complex spatial coherence function based on the principle of van Cittert-Zernike theorem and later it is analysed using a Sagnac radial shearing interferometer with the five-phase shifting algorithm. The object information is computationally acquired on inverse Fourier transform.
Abstract
Introduction
The coherence function at the Fourier plane is given by
From Eq. (1), we can write
Experiment and results
Principle
Conclusion
In the first part of the set up the object information is recorded as a two-point complex spatial coherence function and in the later part a square Sagnac radial shearing interferometer with five-step phase-shifting technique is designed to obtain the complex coherence function.
The digital inverse Fourier transform of complex coherence function helps to retrieve the object information.
Acknowledgments
Akanksha Gautam would like to acknowledge support from DST-INSPIRE (IF180930)
Funding
This work is supported by the Board of Research in Nuclear Sciences (BRNS- Grant No. 58/14/04/2021-BRNS/37092).
Rosen J, Brooker G. Digital spatially incoherent Fresnel holography. Optics letters. 2007 Apr 15;32(8):912-4.
Vijayakumar A, Kashter Y, Kelner R, Rosen J. Coded aperture correlation holography–a new type of incoherent digital holograms. Optics Express. 2016 May 30;24(11):12430-41.
Naik DN, Pedrini G, Osten W. Recording of incoherent-object hologram as complex spatial coherence function using Sagnac radial shearing interferometer and a Pockels cell. Optics Express. 2013 Feb 25;21(4):3990-5.
Hariharan P, Oreb BF, Eiju T. Digital phase-shifting interferometry: a simple error-compensating phase calculation algorithm. Applied optics. 1987 Jul 1;26(13):2504-6.
References
20-22 Feb. 2023