## Slide 1: Assessment of Flood Frequency pattern in a complex mountainous terrain using the SWAT model Simulation
Nada Joumar
Amal Markhi
Jamal Eddine Stitou El Messari
Lahcen Benaabidate
The 7th International Electronic Conference on Water Sciences
Adaptive Water Resources Management in an Era of Changing Climatic, Environmental and Social Conditions
Email: joumarnada@gmail.com

## Slide 2: Summary
Introduction
Material and methods
    Study area description
    SWAT model
        Input data
        Set up
        Calibration
        Results
    3. Flood Frequency Analysis
    Definition
        Results
3. Conclusion

## Slide 3: Introduction
Extreme events such as floods are one of the most dangerous meteorological hazards affecting the Mediterranean countries. N’fis is a typical semi-arid catchment. Flood risk assessment of this type of catchments requires the development/application of modern methodologies, which in many cases, should overcome the lack of suitable field data.
This study includes Hydrological simulation of the N’fis watershed using SWAT model.
Assessment of the flood risk using comparison of the statistical probability distributions, such as Generalized Extreme Value (GEV), Log-Pearson type 3 (LP3), and Gumbel (EV1).

## Slide 4: Material and Methodology
Study area description:
Figure . the location of N’fis watershed and the hydrometeorological stations
N’fis is a subbasin of the Tensift watershed that drains a total area of 1270 km². It is a mountainous watershed located in the part of High Atlas of Marrakech geographic area. More specifically on the northern flank of the central massif west of Toubkal between 30.5 and 31.2 ° North and between longitudes 7, 55 ° and 8, 40 ° W.
The watershed’s elevation ranges from 583 m to 4102 m and a mean elevation of 1868m.

## Slide 5
The watershed is 94% rural land and only 6% urban.
The dominant soil type is zonal brown soils on shale socle (79.3 %)
Figure. Soil map, N’fis watershed.
Figure. Landuse map, N’fis watershed
Notes: area of the basin is rural land and only 6% urban.

## Slide 6
The basin’s general climate is semi-arid, The weather is characterized by hot ( max: 46°) and dry summers then cold (min: -7.4°C) humid winters. The annual rainfall ranges from 254.1mm in low altitude to 796,9mm in high altitudes..
Chart: N'fis annual precipitation
| Janvier | Février | Mars | Avril | Mars | Juin | Juillet | Aout | Septembre | Octobre | Novembre | Decembre
Nkouris | 32.1512 | 32.0252 | 37.6726 | 20.4525 | 11.5537 | 4.2462 | 4.1186 | 8.2366 | 13.0203 | 23.5159 | 34.4161 | 21.325
Imin Lhamam | 42.4659 | 39.8636 | 54.9386 | 55.5 | 29.4227 | 12.1159 | 2.5818 | 4.3535 | 16.5159 | 47.4341 | 41.3591 | 29.95
Barrage Takerkoust | 30.3795 | 28.5386 | 34.1432 | 33.1955 | 16.7545 | 7.4159 | 2.6977 | 4.2 | 10.7205 | 26.0091 | 30.6545 | 20.7182
sidi hssine | 41.1932 | 44.9535 | 42.4769 | 19.5975 | 15.991 | 1.9769 | 1.5544 | 8.1267 | 14.3055 | 26.4509 | 43.7458 | 39.9684
Precipitation mm
Figure. Average annual precipitation in Iguir N’kouris, Immin lhemmam, Lalla Takerkoust and Sidi Hssin
Notes: . The spatio-temporal variability of precipitation is noticeable

## Slide 7
Figure. Location of the Moulay Yacoub and Lalla Takerkoust Dams, N’fis watershed.
Two dams were constructed on N’fis river.
Moulay yacoub el mansour ( 70Mm3) in the upper stream,
Lalla takerkoust (53.6Mm3) downstream at the foothills

## Slide 8: SWAT Model
Continuous, physically based, and semi-distributed Model.
Predict the impact of land management practices on:
The hydrology
Contaminant transport
SWAT subdivides a watershed into subbasin connected by a stream network, and further delineates HRUs (Hydrological response units) consisting of unique combinations of land cover, soils and slopes within each sub-basin.
Sediment yield

## Slide 9
SWt is the soil water content (mm),
SW0 is the water available to plants (mm),
Rday is the daily precipitation (mm),
Qsurf is the surface runoff (mm),
Eα is the evapotranspiration (mm),
Sweep is the percolation (mm),
Qgw is the low flow (mm)
t is the time (days).
Water balance equation:
Figure. Hydrological balance description in SWATcheck.

## Slide 10: Input Data
Data | Source | Spatial resolution | Temporal resolution
DEM | STRM- United States Geological Survey (USGS) https://earthexplorer.usgs.gov/ | 30 m | -
Land use Map | (MODIS) Land Cover Type (MCD12Q1) | 500 m | Yearly
Soil Map | Tensift Basin Hydraulic Agency (TBHA) | ArcInfo format (scale 1:100000) | -
Soil Data | Field work (Markhi et al., 2019) | ArcInfo format (scale 1:100000) | -
Observed Hydrometeorology | Tensift Basin Hydraulic Agency (TBHA) | - | Daily
Table : Geo-spatial datasets.

## Slide 11
Meteorological data
Precipitation 4stations
Temperature 1Station
GIS data
DEM
Soil data
Land use
Observed data
Stream Flow
Setup SWAT model
simulation
Well conducted
Yes
End
No
Calibration using SWAT-Cup, SUFI2
SWAT Model Setup
New parameters

## Slide 12
Calibration Results
Figure. Daily simulated and observed discharge (m³/s) for the period (2002-2012) Iguir Nkouris station.
Figure. Daily simulated and observed discharge (m³/s) for the period (2002-2012) Imin lhemmam station.

## Slide 13
Validation Results
Figure. Daily validated discharge (m³/s) for the period (2013-2016) Iguir Nkouris station.
Figure. Daily validated discharge (m³/s) for the period (2013-2016) Imin Lhemmam station.

## Slide 14
Statistical evaluation parameters | Imin lhemam |  | Nkouris |  | conditions
 | Calibration | Validation | Calibration | Validation | 
NSE | 0.51 | 0.56 | 0.54 | 0.62 | satisfactory >0.5
PBIAS | 16.4 | 15.3 | 22.9 | 21.03 | satisfactory 25%
RMSE | 4.00 | 3.25 | 3.72 | 3.12 | 
Parameter_Name | Description | Rank | Fitted Value | Min value | Max value
CN2.mgt | SCS Curve number | 5 | -0.192 | -0.2 | 0.2
ALPHA_BF.gw | Baseflow factor [days] | 1 | 0.62 | 0 | 1
GW_DELAY.gw | Groundwater delay time (days) | 6 | 424.7 | 30 | 450
GWQMN.gw | Threshold depth of water in the shallow aquifer required for return flow to occur [mm] | 3 | 1.24 | 0 | 2
GW_REVAP.gw | Revap coefficient | 10 | 0.11 | 0 | 0.2
ESCO.hru | Soil Evaporation compensation factor | 4 | 0.87 | 0.8 | 1
EPCO.hru | the plant uptake compensation factor | 16 | 0.96 | 0.8 | 1
CH_N2.rte | Manning's "n" value for the main channel. | 12 | 0.17 | 0 | 0.3
CH_K2.rte | Effective hydraulic conductivity in main channel alluvium. | 2 | 22.5 | 5 | 130
SOL_AWC(1).sol | Available water capacity [mm H2O/mm soil] | 7 | -0.16 | -0.2 | 0.4
SOL_K(1).sol | Saturated hydraulic conductivity parameter | 13 | 0.64 | -0.8 | 0.8
SOL_BD(1).sol | soil bulk density | 14 | -0.3 | -0.5 | 0.6
SFTMP.bsn | Snowfall temperature (°C). | 8 | -4.8 | -5 | 5
SMFMX.bsn | Maximum melt rate for snow during the year | 17 | 7.37 | 1.4 | 7.5
DEEPST.gw | Initial depth of water in the deep aquifer (mm H2O) | 9 | 41000 | 0 | 50000
LAT_TTIME.hru | Lateral flow travel time (days) | 15 | 39.59 | 0 | 180
Table. results of statistical evaluation for the daily calibration
Table. results of best fitted parameters for calibration
Statistical Results

## Slide 15: Flood Frequency analysis
α = shape parameter (α > 0)
β = scale parameter (β ≠ 0)
γ = location parameter
Γ(β) =The Gamma distribution function for the parameter β.
μ = shape parameter (−∞ < α < ∞)
σ = scale parameter (β > 0)
Generalized Extreme Value Distribution (GEV) (3)
σ = scale parameter (σ > 0)
k = shape parameter
μ = location parameter
Extreme events : Floods or Droughts
Magnitude of extreme events is related to their frequency of occurrence.
Log Pearson III
Gumbel (EV I)
50 years of annual discharge (m3 /s) (1966 to 2016) were used for deriving the flood frequency curve by applying the commonly used probability distribution functions which are the Gumbel Distribution (EV), Log Pearson Type 3 and Generalized Extreme Value Distribution (GEV).

## Slide 16
T | log Pearson III | Gumbel | GEV
Kolmogorov-Smirnov | 0.978 | 0.179 | 0.141
Anderson-Darling | -8.009 | 4.524 | 2.763
Table. Goodness-of-fit test result for Imin lhemmam
Figure. Flood frequency analysis Gumbel (EVI), N’fis watershed using data from Imin lhemmam station of the period 1966-2016
Figure. Flood frequency analysis log Pearson III, N’fis watershed using data from Imin lhemmam station of the period 1966-2016
Figure. Flood frequency analysis GEV, N’fis watershed using data from Imin lhemmam station of the period 1966-2016

## Slide 17: Conclusion
The SWAT (Soil and water assessments tool) model managed to simulate adequately the poorly gauged N’fis watershed.
Comparing the goodness‐of‐fit Gumbel, GEV and LP3 distributions for flood frequency analysis in Nfis watershed, the GEV distribution shows good results and appears to be the more suitable one.
For study limitation include the data scarcity and also the SWAT model is not being able to capture the single events and reach the high peaks of flow during dry period. These results are reflected in the statistical evaluation values of the model.
Future scope : the SWAT model is able to help in the sediment yield simulation which can also be used in land management of the watershed.

## Slide 18: Thank you
Email: joumarnada@gmail.com