## Slide 1
Bridging Virtual and Real: Testing Design of Experiment Procedures with Simulated and Experimental Data
Department of Building Materials Technology, Faculty of Materials Science and Ceramics
Akademia Górniczo-Hutnicza im. Stanisława Staszica w Krakowie
AGH University of Kraków
Agnieszka Królicka, Anna Szczurkowska

## Slide 2: Outline
Comparison of Central Composite Design (CCD) and Box-Behnken Design (BBD) using data provided by virtual determination of indium employing ICP-MS TuneSim software
  Response surface profiles
  Predictions versus experimental data
  Optimal parameters
Application of CCD for optimization of real-life experiments
  Optimization of plating process of bismuth film electrode used for voltammetric determination of germanium
  Extraction of Ginkgo biloba to maximise the antioxidant properties of the resultant infusion

## Slide 3: IC – MS
Optimization of ICP torch position – Virtual experiments employing IC-MS TuneSim software

## Slide 4: ICP-MS TuneSim software
Torch position
X – from -4.5 to 4.5 mm
Y – from -4.5 to 4.5 mm
Z – from -2.5 to 2.5 mm
Analyte – 115In
J. Chem. Educ. 2018, 95, 11, 2059–2063

## Slide 5: Torch position
https://twitter.com/Tecplot/status/1063532269481144321
ICP – MS
torch
0
1
-1
1.68
-1.68
1.12
1.8
2.8
3.8
4.48
x, y
Coded
Uncoded
(mm)
0
1
-1
1.68
-1.68
-0.88
-0.2
0.8
1.8
2.48
z
Coded
Uncoded
(mm)
For 3 factors (x,y,z):   1.68
- star points

## Slide 6: Box-Behnken Design
BBD

## Slide 7: Box-Behnken Design BBD 1
X (mm) | 3.2
Y (mm) | 3.0
Z (mm) | 0.3
Intensity (cps) predicted | 10463±346
Intensity (cps) measured | 10417±43
z = 0.3 mm

## Slide 8: BBD 1
Design | X (mm) | Y (mm) | Z (mm) | Intensity (cps)
1 | 1.8 | 1.8 | 0.8 | 4912.00
11 | 2.8 | 1.8 | 1.8 | 5763.00
13 | 2.8 | 2.8 | 0.8 | 10372.00
6 | 3.8 | 2.8 | -0.2 | 9480.00
5 | 1.8 | 2.8 | -0.2 | 6550.00
15 | 2.8 | 2.8 | 0.8 | 9864.00
3 | 1.8 | 3.8 | 0.8 | 5148.00
2 | 3.8 | 1.8 | 0.8 | 6435.00
17 | 2.8 | 2.8 | 0.8 | 9835.00
14 | 2.8 | 2.8 | 0.8 | 9769.00
12 | 2.8 | 3.8 | 1.8 | 7115.00
8 | 3.8 | 2.8 | 1.8 | 7729.00
10 | 2.8 | 3.8 | -0.2 | 9265.00
16 | 2.8 | 2.8 | 0.8 | 9906.00
9 | 2.8 | 1.8 | -0.2 | 7465.00
7 | 1.8 | 2.8 | 1.8 | 5191.00
18 | 2.8 | 2.8 | 0.8 | 9746.00
4 | 3.8 | 3.8 | 0.8 | 8806.00
N = 2k(k+1) + N0

## Slide 9: Box-Behnken Design BBD 2
X (mm) | 3.2
Y (mm) | 3.0
Z (mm) | 0.1
Intensity (cps) predicted | 10496±3472
Intensity (cps) measured | 10506±65
z = 0.1 mm

## Slide 10: BBD 2
Design | X (mm) | Y (mm) | Z (mm) | Intensity (cps)
17 | 2.8 | 2.8 | 0.8 | 9767.00
11 | 2.8 | 1.8 | 1.8 | 5746.00
2 | 3.8 | 1.8 | 0.8 | 6496.00
15 | 2.8 | 2.8 | 0.8 | 9800.00
1 | 1.8 | 1.8 | 0.8 | 4873.00
13 | 2.8 | 2.8 | 0.8 | 9941.00
4 | 3.8 | 3.8 | 0.8 | 8814.00
8 | 3.8 | 2.8 | 1.8 | 7780.00
16 | 2.8 | 2.8 | 0.8 | 9877.00
3 | 1.8 | 3.8 | 0.8 | 5121.00
10 | 2.8 | 3.8 | -0.2 | 9244.00
14 | 2.8 | 2.8 | 0.8 | 9847.00
18 | 2.8 | 2.8 | 0.8 | 9667.00
6 | 3.8 | 2.8 | -0.2 | 9984.00
7 | 1.8 | 2.8 | 1.8 | 5215.00
5 | 1.8 | 2.8 | -0.2 | 6671.00
12 | 2.8 | 3.8 | 1.8 | 7111.00
9 | 2.8 | 1.8 | -0.2 | 7419.00

## Slide 11: Box-Behnken Design BBD 3
X (mm) | 3.2
Y (mm) | 3.0
Z (mm) | 0.2
Intensity (cps) predicted | 10458±354
Intensity (cps) measured | 10432±54
z = 0.2 mm

## Slide 12: BBD 3
Design | X (mm) | Y (mm) | Z (mm) | Intensity (cps)
6 | 3.8 | 2.8 | -0.2 | 9909
5 | 1.8 | 2.8 | -0.2 | 6664
10 | 2.8 | 3.8 | -0.2 | 9264
2 | 3.8 | 1.8 | 0.8 | 6449
13 | 2.8 | 2.8 | 0.8 | 9795
7 | 1.8 | 2.8 | 1.8 | 5200
8 | 3.8 | 2.8 | 1.8 | 7666
3 | 1.8 | 3.8 | 0.8 | 5192
11 | 2.8 | 1.8 | 1.8 | 5700
12 | 2.8 | 3.8 | 1.8 | 7192
14 | 2.8 | 2.8 | 0.8 | 9830
15 | 2.8 | 2.8 | 0.8 | 9831
4 | 3.8 | 3.8 | 0.8 | 8729
1 | 1.8 | 1.8 | 0.8 | 5101
17 | 2.8 | 2.8 | 0.8 | 9882
18 | 2.8 | 2.8 | 0.8 | 9916
16 | 2.8 | 2.8 | 0.8 | 9721
9 | 2.8 | 1.8 | -0.2 | 7414

## Slide 13: Box-Behnken Design BBD 1 - incorrect data
X (mm) | 2.9
Y (mm) | 3.4
Z (mm) | 0.9
Intensity (cps) predicted | 10162
z = 0.9 mm
Poor correlation

## Slide 14: BBD 1 – with incorrect data
Design | X (mm) | Y (mm) | Z (mm) | Intensity (cps)
1 | 1.8 | 1.8 | 0.8 | 4912.00
11 | 2.8 | 1.8 | 1.8 | 5763.00
13 | 2.8 | 2.8 | 0.8 | 10372.00
6 | 3.8 | 2.8 | -0.2 | 948.00
5 | 1.8 | 2.8 | -0.2 | 6550.00
15 | 2.8 | 2.8 | 0.8 | 9864.00
3 | 1.8 | 3.8 | 0.8 | 5148.00
2 | 3.8 | 1.8 | 0.8 | 6435.00
17 | 2.8 | 2.8 | 0.8 | 9835.00
14 | 2.8 | 2.8 | 0.8 | 9769.00
12 | 2.8 | 3.8 | 1.8 | 7115.00
8 | 3.8 | 2.8 | 1.8 | 7729.00
10 | 2.8 | 3.8 | -0.2 | 9265.00
16 | 2.8 | 2.8 | 0.8 | 9906.00
9 | 2.8 | 1.8 | -0.2 | 7465.00
7 | 1.8 | 2.8 | 1.8 | 5191.00
18 | 2.8 | 2.8 | 0.8 | 9746.00
4 | 3.8 | 3.8 | 0.8 | 8806.00
incorrect

## Slide 15: Central Composite Design

## Slide 16: Central Composite Design CCD - centred star points
X (mm) | 3.3
Y (mm) | 3.1
Z (mm) | -0.9
Intensity (cps) predicted | 10837±1160
Intensity (cps) measured | 11877±65
z = -0.9 mm

## Slide 17: CCD - centred star points
Design | X (mm) | Y (mm) | Z (mm) | Intensity (cps)
3 | 1.8 | 3.8 | -0.2 | 5529
17 (C) | 2.8 | 2.8 | 0.8 | 9920
14 | 2.8 | 2.8 | 1.8 | 8075
10 | 3.8 | 2.8 | 0.8 | 9261
16 (C) | 2.8 | 2.8 | 0.8 | 9785
11 | 2.8 | 1.8 | 0.8 | 7042
6 | 3.8 | 1.8 | 1.8 | 5232
1 | 1.8 | 1.8 | -0.2 | 5137
7 | 3.8 | 3.8 | -0.2 | 9288
9 | 1.8 | 2.8 | 0.8 | 6301
2 | 1.8 | 1.8 | 1.8 | 4067
13 | 2.8 | 2.8 | -0.2 | 10486
12 | 2.8 | 3.8 | 0.8 | 8607
4 | 1.8 | 3.8 | 1.8 | 4260
18 (C) | 2.8 | 2.8 | 0.8 | 9952
15 (C) | 2.8 | 2.8 | 0.8 | 9691
8 | 3.8 | 3.8 | 1.8 | 7167
5 | 3.8 | 1.8 | -0.2 | 6904
19 (C) | 2.8 | 2.8 | 0.8 | 9804

## Slide 18: Central Composite Design CCD
X (mm) | 3.3
Y (mm) | 3.2
Z (mm) | -0.9
Intensity (cps) predicted | 11043±1098
Intensity (cps) measured | 11879±69
z = - 0.9 mm

## Slide 19: CCD
Design | X (mm) | Y (mm) | Z (mm) | Intensity (cps)
13 | 2.8 | 2.8 | -0.9 | 11455
5 | 3.8 | 1.8 | -0.2 | 6673
11 | 2.8 | 1.1 | 0.8 | 4249
9 | 1.1 | 2.8 | 0.8 | 3516
1 | 1.8 | 1.8 | -0.2 | 5148
12 | 2.8 | 4.5 | 0.8 | 7120
8 | 3.8 | 3.8 | 1.8 | 7135
15 (C) | 2.8 | 2.8 | 0.8 | 9926
3 | 1.8 | 3.8 | -0.2 | 5524
19 (C) | 2.8 | 2.8 | 0.8 | 9833
18 (C) | 2.8 | 2.8 | 0.8 | 9644
17 (C) | 2.8 | 2.8 | 0.8 | 9703
7 | 3.8 | 3.8 | -0.2 | 9365
2 | 1.8 | 1.8 | 1.8 | 4032
14 | 2.8 | 2.8 | 2.5 | 7132
16 (C) | 2.8 | 2.8 | 0.8 | 9801
6 | 3.8 | 1.8 | 1.8 | 5311
10 | 4.5 | 2.8 | 0.8 | 7627
4 | 1.8 | 3.8 | 1.8 | 4262
N = 2k + 2k + N0
z
z
x
y
y
x

## Slide 20: BBD versus CCD optimization of torch position
virtual determination of In by ICP-MS
Intensity of indium signal obtained after optimisation performed by BBD and CCD

## Slide 21: Bismuth plating
Preparation of bismuth film electrode for catalytic adsorptive stripping voltammetry – real experiments

## Slide 22: Central Composite Design CCD - centred star points
Eplat (V) | -1.156
Q (mC) | 42.8
C (mM) | 16.7
Peak current (µA) predicted | 5.42±0.48
cBi = 16.7 mM

## Slide 23: CCD BiFE
Design | Eplat (V) | Q (mC) | C (mM) | Peak current (µA)
1 | -0.9 | 10.0 | 13.0 | 3.80
2 | -0.9 | 10.0 | 43.0 | 2.70
3 | -0.9 | 50.0 | 13.0 | 4.70
4 | -0.9 | 50.0 | 43.0 | 6.00
5 | -1.5 | 10.0 | 13.0 | 4.10
6 | -1.5 | 10.0 | 43.0 | 5.00
7 | -1.5 | 50.0 | 13.0 | 4.70
8 | -1.5 | 50.0 | 43.0 | 5.80
9 | -0.9 | 30.0 | 28.0 | 4.40
10 | -1.5 | 30.0 | 28.0 | 5.10
11 | -1.2 | 10.0 | 28.0 | 4.00
12 | -1.2 | 50.0 | 28.0 | 5.30
13 | -1.2 | 30.0 | 13.0 | 5.30
14 | -1.2 | 30.0 | 43.0 | 5.30
15 (C) | -1.2 | 30.0 | 28.0 | 5.00
16 (C) | -1.2 | 30.0 | 28.0 | 4.95

## Slide 24: Extraction of antioxidants from herbs
Optimisation of temperature and time for Ginkgo biloba infusions – real experiments

## Slide 25: Voltammetry of Ginkgo biloba infusions
0.15 g/ 50 g water
75C, 11.7 min
(point 8th of design table)
0.15 M acetic acid, GC 3 mm,
Eacc = 0 V, t = 5 s, 0.1 V/s (CV), E = 50 mV (DPV)

## Slide 26: Central Composite Design CCD
Temperature (C) | 98.5
Time (min) | 16.5
Design | Temperature (C) | Time (min) | Peak current (µA)
5 | 53.8 | 6.0 | 0.11
13 (C) | 75.0 | 6.0 | 0.21
2 | 60.0 | 10.0 | 0.18
6 | 96.2 | 6.0 | 0.19
8 | 75.0 | 11.7 | 0.26
4 | 90.0 | 10.0 | 0.26
3 | 90.0 | 2.0 | 0.15
10 (C) | 75.0 | 6.0 | 0.15
7 | 75.0 | 0.3 | 0.05
9 (C) | 75.0 | 6.0 | 0.20
12 (C) | 75.0 | 6.0 | 0.21
1 | 60.0 | 2.0 | 0.11
11 (C) | 75.0 | 6.0 | 0.21

## Slide 27: Conclusions
Virtual experiments using the ICP-MS TuneSim software yield useful results that can be used as test data to assess the applicability of various design of experiments (DOE) procedures and DOE software.
The central composite design (CCD) provided superior results compared to the Box-Behnken design (BBD), without a significant increase in the number of measurements
  For 3 factors + 3 additional central points: 19 for CCD vs. 18 for BBD.
The expertise in DOE acquired during virtual experiments can be successfully implemented in real-life experiments in the field of analytical chemistry.

## Slide 28: Thank you for your attention!