## Slide 1: 1st International Online Conference on Buildings Online, 24–26 Oct 2023
Research on Asymmetrical Concrete Low-Rise Frames
Under Multiple Seismic Events
Paraskevi K. Askouni
Adjunct Lecturer, Department of Civil Engineering, University of Patras, Greece
askounie@upatras.gr

## Slide 2
Geometrical structural asymmetry is mentioned to influence the seismic response in existing research, e.g. in Rutenberg [1], Goel and Chopra [2] and Bento et al. [3]. Besides plenty of research is already performed on reinforced concrete common buildings, dimensioned to current regulations such as Eurocode 2 (EC2) [4] following the seismic guidelines of Eurocode 8 (EC8) [5].
However, the current seismic design codes, e.g. EC8 [5], tend to ignore the role of multiple seismic events on the structural response, though identified by other research works, such as Refs. [6-8].
The current paper aims to point out the significance of multiple ground excitation events on the behavior of common, symmetric/asymmetric low-rise 3D frames.
INTRODUCTION

## Slide 3
DESCRIPTION OF FRAMES AND ANALYSIS
Asymmetrical RC buildings with ( a ) one story and ( b ) three stories.

## Slide 4
The investigated one- and three-story frames have in-plan dimensions of 5.0 × 4.0 m2. The first story has a height of 4.0 m, while the second and third ones possess a height of 3.0 m each. The RC beams have sectional dimensions as 0.25 × 0.60 m2. The three RC columns have a the same dimensions, as 0.40 × 0.40 m2 at the first story and 0.35 × 0.35 m2 at upper ones, while the fourth column has an in-steps-variable cross-section from the previous values up to 0.30 × 2.0 m2, called here as “wall”.
The examined buildings are constructed by concrete C20/25 reinforced with steel B500c, designed and detailed following the current codes, EC2 [4], and EC8 [5], where the considered loadings follow Eurocode 1 [9] and their combinations are according to [5] considering the characteristic 30% provision [5] and the “accidental eccentricity” of 5% [5}. The dimensioning and design assumptions consider typical domestic buildings for a ductility class medium [DCM) [4-5], zone ground acceleration 0.36g, 5% viscous damping ratio, soil type C, and the usual rigid soil assumption. The behavior factor [5] of each frame is estimated separately according to current codes. The capacity design rules of EC2 [4], and EC8 [5] are considered in the detailing of main structural elements and their connections against “shear” [5].
DESCRIPTION OF FRAMES AND ANALYSIS

## Slide 5
The “non-linear time-history (NLTH) analyses” [10] are accomplished using the software ETABS [11] for the following multiple 3D seismic events, as downloaded from PEER [12]:
“Chalfant Valley” [12], in 1986, characterized by 2 events;
the “Coalinga”[12], in 1983, by 2 events;
“Imperial Valley” [12], in 1979, by 2 events;
“Mammoth Lakes” [12], in 1980, by 5 events; and
“Whittier Narrows” [12], in 1987, by 2 events. Similarly, to [6,7,10],
for each ground motion, between the seismic events, a time-frame of 100s with acceleration values equal to zero is considered to calm down the structural vibration caused by damping.
In addition, the frames are analyzed under the first excitation of the “Mammoth Lakes” excitation, referred to here as “Mammoth-1st”, to compare the effect of one event to multiple ones.
The angle of the earthquake direction is chosen as “θ=0⁰, θ=90⁰ and θ=45⁰” [10], corresponding to the basic horizontal and the diagonal axes
DESCRIPTION OF FRAMES AND ANALYSIS

## Slide 6
The asymmetry of the frames is induced by the asymmetry of the wall element compared to the column, where a division of the later sections provides a simple dimensionless ratio, mentioned here as “A(wall)/(col)”.
Due to limited space, selected charts are shown regarding the “interstory drift ratio” (“IDR”) [10,16] and the “residual IDR” (“RIDR”) [10] comparatively to the constraints of the “performance levels” [16] for reinforced concrete buildings.
For reading convenience, there are mentioned the limits of IDR as 0.01 corresponding to the “Immediate Occupancy (IO)” “performance level” [16], 0.02 to the “Life Safety (LS) performance level” [16], and 0.04 to the “Collapse Prevention (CP) performance level” [16].
Respectively, the RIDR limits are mentioned as negligible for the IO stage [16], 0.01 for the LS stage [16], and 0.04 for the CP stage [16].
SEISMIC RESPONSE RESULTS

## Slide 7
SEISMIC RESPONSE RESULTS
One-Story Frames
(a) Interstory drift ratio on X, θ=45°, (b) Interstory drift ratio on Y, θ=0°.

## Slide 8
SEISMIC RESPONSE RESULTS
(a) Residual interstory drift ratio on X, θ=90°, (b) Residual interstory drift ratio on Y, θ=90°.

## Slide 9
SEISMIC RESPONSE RESULTS
Three-Story Frames
(a) Interstory drift ratio on X axis, θ=0°, (b) Interstory drift ratio on Y axis, θ=90°, 1st story

## Slide 10
SEISMIC RESPONSE RESULTS
(a) Interstory drift ratio on X axis, θ=0°, (b) Interstory drift ratio on Y axis, θ=90°, 2nd story.

## Slide 11
SEISMIC RESPONSE RESULTS
(a) Interstory drift ratio on X axis, θ=90°, (b) Interstory drift ratio on Y axis, θ=90°, 3rd story.

## Slide 12
SEISMIC RESPONSE RESULTS
(a) Residual interstory drift ratio on X axis, θ=45°, (b) Residual interstory drift ratio on Y axis, θ=45°, 1st story

## Slide 13
SEISMIC RESPONSE RESULTS
(a) Residual interstory drift ratio on X axis, θ=45°, (b) Residual interstory drift ratio on Y axis, θ=0°, 3rd story.

## Slide 14
The IDR increases with larger wall sections, and in addition for higher building frames. In general, the IDR charts tend to have a value range inside the allowed limits of the present seismic regulations.
The RIDR charts have a general value range inside the allowed constrains of the applicable regulations. The RIDR values for the Y axis are noticed as greater than the corresponding ones for the X axis.
The direction of the ground excitation influences the seismic response characteristics, while the selected values of 0°, 45°, and 90° are identical for the definition of the most detrimental response values.
The multiple seismic events tend to deteriorate the strength of RC frames.
The framed constructions with large wall cross-sections, i.e., greater than the “wall” limit section of present provisions, as well as the symmetrical buildings, are vulnerable to multiple seismic events, in contrast to a single seismic excitation.
CONCLUSIONS

## Slide 15
Thank you for your attention!
1st International Online Conference on Buildings Online, 24–26 Oct 2023