## Slide 1: A High Efficient Cross Connected H-bridge Style Multilevel Inverter with Lower Power Components
AUTHORS:
Dr. L VIJAYARAJA , DEEE , SRI SAIRAM INSTITUTE OF TECHNOLOGY
Dr. R DHANASEKAR, DEEE , SRI SAIRAM INSTITUTE OF TECHNOLOGY
Mr. S KESAV SANADHAN, DEEE , SRI SAIRAM INSTITUTE OF TECHNOLOGY
Mrs. RUPA KESAVAN, DCSE, SRI VENKATESHWARA COLLEGE OF ENGINEERING
The 4th International Electronic Conference on Applied Sciences

## Slide 2: OBJECTIVE
1
The main purpose of a multilevel
inverter is to provide sinusoidal
waveforms with low-level harmonic
content
2
To improve the efficiency
of the inverter
3
To reduce distortion in a
grid

## Slide 3: ABSTRACT
Compare to the classical inverters, the multilevel inverter finds remarkable advantages, which can be suitably implemented in green energy power generation.
The proposed inverter is constructed in real-time, and the performance of the inverter is studied by testing with fixed and variable reactive loads.
An asymmetric multilevel inverter with fewer components is proposed for renewable energy applications. The proposed inverter is a cross between two H bridge-style devices
03
01
02

## Slide 4: PROPOSED SOLUTION
5
The inverter produces higher efficieny and low THD .
3
The proposed inverter uses Nearest Level Modulation Technique as controller
1
The proposed Multilevel Inverter converts the DC source to AC source.
4
The inverter is connected to the grid.
2
It produces the 19 levels of output voltage and simulated using matlab software.

## Slide 5: CIRCUIT DIAGRAM
The proposed asymmetric multilevel inverter structure is shown in the figure 1. The inverter consists of three asymmetric sources and 12 power electronic switches. The proposed inverter produces 19 levels of output voltage and the inverter is controlled by the Nearest Level Modulation (NLM) technique. The unequal DC magnitude i.e, V1 = VDC, V2 = 3VDC, V3 = 5VDC, the configured inverter produces 9 +ve voltage levels , 9 –ve voltage levels and with zero voltage level.

## Slide 6: HARWARE MODEL
The prototype of proposed inverter. The inverter receives pulses from the edge control mechanism. The program is flased to the controller using FGPA controller. The IGBT devices are used as switches. The four stepdown transformers are used to stepdown the grid voltage and fed to the driver circuits. The driver circuits are used to drive the 12 IGBT switches. The protoype is validated with variable and fixed resistive, impedance loads.
FIG 1 HARDWARE MODEL
FIG 2 VOLTAGE WAVEFORM

## Slide 7: THANK YOU