## Slide 1
Artificial intelligence and optimisation computing to lead energy retrofit programs in complex real estate investments
Aurora Greta Ruggeri, Laura Gabrielli and Massimiliano Scarpa

## Slide 2: Topic of interest
Planning Energy retrofit actions in wide building stocks
Elaborate a decision-making model for energy retrofit in property portfolios to achieve the optimal allocation of financial resources under a multi-objective perspective (environmental, social, economic, cultural..), within given constraints (budget, feasibility..)
Topic
Goal
integration of artificial intelligence and optimisation computing to sustain energy retrofit investments in complex real estate assets
DECISION SUPPORT SYSTEM

## Slide 3: Research questions
How can we handle energy retrofit operations at the stock level, managing a huge number of properties at a time, addressing the problems of:
Buildings’ energy demand assessment;
Identification of the optimal outcome while considering multiple objectives and constraints;
Evaluation of the risk around the result
Energy assessment
Retrofit
actions
Assessment criteria
Optimization
Risk and uncertainty
Lack of a shared methodology to assess energy consumption at a portfolio level: fast, reliable, not excessively data-demanding
Lack of a shared methodology to allocate resources at a portfolio level considering multiple objectives, within given constraints
Lack of a shared methodology to “quantify” risk for energy retrofit operations at a portfolio level (sources of uncertainty)
Literature gaps
RQs
Lack of automated calculation procedures in order to jump from the single-building perspective to a stock-based one, and that allow comparing a huge amount of retrofit scenarios

## Slide 4: Method: general approach
Optimal configuration
Retrofit options
Evolutive algorithm
NEURAL NETWORKS
Energy consumption pre-retrofit
Energy Savings
Retrofit scenarios
Risk and uncertainty analysis
Monetary Savings
Restoration Score
ANALYTIC HIERARCHY PROCESS
MAXIMUM BENEFIT

## Slide 5: Energy assessment with the Artificial Neural Networks
OUTPUT NEURON
X1
X2
…
Xr
XR
…
…
…
Yforecast
HIDDEN LAYERS
INPUT NEURONS
Buindings’ information
Energy consumption
DATABASE PRODUCED
100,000 parametric simulations
Development of the NEURAL NETWORKS
The first problem the research faces is the assessment of energy-uses and energy-efficiency potentials for a building asset counting a plethora of premises, which ends up being a problem of mass-appraisal and screening evaluation. To address this first issue, 100,000 parametric simulations are run in Energy Plus.

## Slide 6
Producing the training database
to develop the Artificial Neural Networks
Geometry
Envelope
Orientation
Climatic Area
Exposure
Installations
Use and Schedule
DATABASE PRODUCED
Yearly Primary Energy Demand
Parametric building characteristics
INPUTS
100,000 parametric simulations
Development of the NEURAL NETWORKS
OUTPUT
Such simulations associate the varying building’s characteristics (envelope, installations, dimension, etc.) to the corresponding primary energy consumption.

## Slide 7: A case-study in Italy
BkSm
building
scenario
Bk, k ∈ N {1, …, 11},
Sm, m ∈ N {1, …, M}.
a total of 1,11504E+43 scenarios can be generated !!!
All the possible combinations of energy retrofit interventions (Scenarios)
The pilot case-study is a small portfolio of residential buildings in Bologna, Northern Italy.
The portfolio analysed involves eleven residential buildings built in Bologna between years 1950 - 1990.
Bk, k ∈ N {1, …, 11},
11 buildings Bk 
Sm, m ∈ N {1, …, M},
M retrofit Scenarios Sm 

## Slide 8: Three decision-making criteria
To understand which could be the best retrofit scenario to be implemented on every building of a stock, three performance indexes are introduced.
The three indexes measure the impact produced in terms of energy, monetary and architectural aspects.
The energy savings (ES) are assessed using the neural networks, comparing the energy consumption before and after the retrofit.
The net monetary savings (NS) are estimated based on a Life Cycle Costing approach.
The architectural compatibility of the retrofit measure on the building is assessed by means of an Analytic Hierarchy Process allowing the assessment of a restoration score (RS).
Energy Savings
Monetary Savings
Restoration Score

## Slide 9: 1st decision-making criterion: Energy Savings (ES)
The environmental benefits are given as the energy saved (ES) per year (kWh/m²·y). The ESm parameter measures the yearly primary energy demand for space heating/cooling, hot water and lighting (YEDm) saved after the implementation of any mth scenario if compared to the as-is status.
∀ Bk, k ∈ N {1, …, 11}
∀ Sm, m ∈ N {1, …, M}  ∀ BkSm
HEATING
COOLING

## Slide 10: 2nd decision-making criterion: Net Savings (NS)
The NSm are simply the difference in the LCC pre and post retrofit. The NS are assessed over a period of 30 years:
∀ Bk, k ∈ N {1, …, 11}
∀ Sm, m ∈ N {1, …, M}  ∀ BkSm
t ∈ N {0, …, 30}
s ∈ N {0, …, 10}
Economic variables

## Slide 11: 3rd decision-making criterion: Restoration score (RS)
Retrofit 1
Retrofit n
Retrofit 2
Restoration Score
Reversibility
Distinguishability
Authenticity
Compatibility
Minimum Intervention
Visual Impact
OBJECTIVE
CRITERIA
ALTERNATIVES
………….
Retrofit n-1
AHP
A commission of 10 experts evaluates the retrofit options according to the principles of restoration
The restoration score is assessed through an Analytic Hierarchy Process. Each retrofit option is assigned a score that reflects the compatibility of interventions
0% <= <= 100%
= function (AHP)
∀ Bk, k ∈ N {1, …, 11}
∀ Oq, q ∈ N {1, …, 18} e
Ω = {O1, …, Oq, …, O18}
∀ Sm, m ∈ N {1, …, M}
con Sm = ∀ ⊂ ∨ ⊆ Ω
 ∀ BkSm

## Slide 12: Multi attribute optimization
∀ k  (BkSm_opt), Sm_opt is the optimal set of retrofit options
∀ Bk, k ∈ N {1, …, 11}
∀ Sm, m ∈ N {1, …, M}  ∀ BkSm
Xk,m ∈ N {0,1} = binary decision variable
Weighs are assessed by the 10 experts through an AHP
After the three decisional indexes ES; NS; RS are established, an evolutionary algorithm is launched to test out the overall benefits produced by every scenario if applied to the buildings of a stock and select the best scenario
The algorithm iteratively calculates the indexes for every scenario of intervention inside the feasibility domain, as a sum of the benefits/costs for each building.
The target is the optimal configuration of interventions over the stock, i.e. the one that simultaneously maximizes the three indexes, within the declared constraints.

## Slide 13: Identification of the optimal solution
The optimization is solved through an evolutionary algorithm that tests all the feasible combinations building-scenario (Bk Sm) and stops when the optimum is found.
Multi attribute optimization
1,11504E+43 combinations
BkSm
Evolutive algorithm
11 buildingsBk
18 scenarios Sm
Neural networks
Automated calculation
Python Code
Iterative assessment of the indexes ESk,m, NSk,m, RSk,m
Optimal solution
∀ k  BkSm_opt

## Slide 14: Results: The Optimal Configuration
Considering the building portfolio as a whole, the investment cost to implement the energy retrofit measures on the eleven buildings is 2,955,063 €, while the produced net saving after a 30-year timeframe is 2,010,305 €.
The overall economic valuation on the entire stock is finally performed through a Discounted Cash Flow analysis (DCFA). It is chosen to prioritize the interventions according to their effectiveness, and a cost-effectiveness index is defined as ESk,m_opt/Cik,m_opt
t ∈ N {0, …, 30}
s ∈ N {0, …, 10}
k ∈ N {1, …, 11}
m ∈ N {0, …, M}
As a result, after a 30-year period of analysis, the NPV of cash flows is 1,831,870 €, representing the economic net benefit of the investment over the stock.
The payback period is at year 12, while the IRR is 10.64%.

## Slide 15: Risk and Uncertainty
In the final part of the research, a risk analysis studies how the uncertainty factors may impact the results of the chosen configuration of interventions.
Mean | 
Median | 
Mode | 
Standard Deviation | 
Skewness | 
Kurtosis | 
Minimum | 
Maximum | 
Range | 
1,671,546
1,690,936
---
227,760
-0.289
2.58
838,973
2,378,253
1,539,280
MONTE CARLO SIMULATION: OUTPUT
Similar
Higher
Wider
NPV (€)

## Slide 16: Contribution and Research opportunities
Private stakeholders, Public Administrations, real estate companies, asset holders or portfolio managers need reliable decision support systems to select the most cost-effective retrofit solutions to implement
Experiment the effectiveness of a flexible decision support system that helps asset holders to evaluate specific, reliable and robust actions to enhance existing building portfolios, optimizing their cash flows
Research
contribution
Fill the lack emerged by the literature of an acknowledged methodology to deal with energy retrofit in wide building stocks, overcoming the single-building perspective
Research
opportunities
Implication for
practice

## Slide 17: Thank You for Your attention