## Slide 1: Development and Evaluation of a New Temperature Effect Removal Algorithm for AMSR2 Satellite Soil Moisture Product using Brightness Temperature
Agampodi Deva Thisaru Nayanathara Kumarasiri, Minjiao LU and Kim Oanh Hoang
Nagaoka University of Technology, Japan
Department of Civil and Environmental Engineering

## Slide 2: Content
The current methods to estimate the soil moisture
Existence of Temperature Effect (TE) in in-situ and satellite Soil Water Content (SWC) data
Objectives
Study Area and data description
Methodology
Application
Results

## Slide 3: The current methods to estimate the soil water content
Soil Moisture Methods
Satellite remote sensing observation
Neutron probe technology
The gravimetric method (oven drying)
Dielectrically measured methods
Soil moisture estimating models
Time Domain Reflectometry sensors (TDR)
Capacitance and Frequency Domain Reflectometry sensors (FDR)
Ground based techniques
Agricultural monitoring
Drought and flood forecasting
Forest fire prediction
Water supply management
Importance of satellite observation soil moisture
Examples for satellite that used to obtain soil moisture: SMMR, AMSR-E, SMOS, SMAP, AMSR2

## Slide 4: Existence of Temperature Effect (TE) in in-situ and satellite Soil Water Content (SWC) data
Chart: Time of the days
(Yamamato and Lu, 2022)
Areal mean of in-situ SWC, soil temperature, SMAP SWC at ascending and descending times and SMAP surface temperature at Oklahoma, USA (Hoang and Lu (2021))
Satellite soil water content products
Horizontal insertion
Vertical insertion
Volumetric SWC
Soil temperature

## Slide 5: Problem Statement
Satellite data used the same physical base as in-situ data, the bulk dielectric constant;
Satellite data used in-situ soil moisture as the ground truth for calibration and validation process
The impact and removal of temperature effects on satellite soil water content (AMSR2) still need to be evaluate

## Slide 6
Confirmation of the temperature effect on AMSR2 SWC data
Develop the new temperature effect removal method which is suitable for satellite SWC data
Evaluate the impact of that correction in AMSR2 satellite soil water content data
Objectives

## Slide 7: Study area and data description
In-situ data
3cm depth soil water content and soil temperature were selected
Accessed from the website of GCOM-W1 Research Product Distribution Service (https://suzaku.eorc.jaxa.jp/GCOM_W/research/resdist.html)
Only 9 stations have been selected from 5th Sep, 2016 to 31st Oct, 2019
The in-situ data has been weighted by using Thiessen polygon method correspond to the resolution of satellite data
Satellite data
AMSR2 level 2 soil moisture product at 50km X 50km / 0.5 x 0.5 degree spatial resolution
Obtained from the G-Portal System website (https://gportal.jaxa.jp/gpr/search?tab=0)
Local crossing times AMSR2 are around 1:30p.m. and 1:30a.m. respectively for ascending and descending over passes.
Station name | Station ID | Network | Weighing
ASSH820 | C2 | ASSH | 0.204038
ASSH815 | C4 | ASSH | 0.158021
ASSH8122 | A3E | ASSH | 0.129942
ASSH817 | D1 | ASSH | 0.107943
ASSH813 | E4 | ASSH | 0.155352
ASSH819 | A6 | ASSH | 0.022081
ASSH811 | F2 | ASSH | 0.114076
MGS |  | AWS | 0.06894
DRS |  | AWS | 0.039608
Study area: Mongolia

## Slide 8: Methodology
Analyzing the trend of Ascending (ASC) and Descending (DES) crossing time soil water content from both satellite and in-situ observation
Analyzing and developing the temperature effect error removal method for satellite soil water content products
Applying the temperature effect removal method to confirm and evaluate the impacts of these effects on satellite SWC data

## Slide 9: Temperature effect removal in in-situ data
The data- driven method (Lu et al., 2015 )
The correction equation
. It is considered the calibration curve will give correct value.
For satellite data, only ASC and DES data are available.
It is difficult to estimate amplitudes.
Following changes should be considered.
 Change of SWC
 Change of T
 Mean SWC
Application of the automated temperature effects removal (Kapilaratne and Lu, 2017, 10.1016/j.jhydrol.2017.05.050) to in-situ data.

## Slide 10: Temperature effect removal in satellite data
Triangle method for satellite data
The correction equation for satellite data
Temperature data:
Using soil temperature as a surrogate at development stage
Using satellite surface temperature product or brightness temperature
Calculation of difference:
asc : ascending des : descending
p : previous f : following

## Slide 11
Chart: Ratio of SWC
| ASC P/D | D/D | ASC F/D
SWC | 1.1778 | 1 | 1.1108
SWC_Am | 1.1443
TS | 1.0521 | 1 | 1.0525
TS_Am | 1.0523
The summarization of the trend of normalized ASC and DES soil water content and soil temperature data of AMSR2
ASC P : Ascending Previous
D : Descending
ASC F : Ascending Following
TE
Temperature data:
Using soil temperature as a surrogate at development stage
Using soil temperature, surface temperature and satellite brightness temperature product
Calculation of difference:
asc: ascending des : descending
p : previous f : following
Temperature effect removal in satellite data cont.
Where m means average of previous and following ascending

## Slide 12: Brightness Temperature (TB)
Satellite observation
Basing on the dependency of the microwave measurement on the dielectric properties
(1)
Reasons for using Brightness Temperature (TB)
Brightness temperature is a basic observable quantity calculated from the antenna temperature of a microwave radiometer.
Can be directly measure from the satellite
Surface temperature can be obtained through the brightness temperature
(2)

## Slide 13: Application: Temperature effect removal
Applying newly developed method to satellite SWC products using brightness temperature (TB)
Results and effects of temperature effect error removal for satellite data
Finding the temperature effect coefficient (α)

## Slide 14: Application: Temperature effect removal Cont.
Accumulation of absolute error in satellite soil moisture data

## Slide 15: Results of temperature effect removal
A diagram of after removing the TE on AMSR2 satellite SWC data by using brightness temperature data (TB)
A diagram of original and corrected AMSR2 ASC and DES SWC data

## Slide 16: Conclusion
Found the temperature effect also exist in the AMSR2 SWC data
Temperature effect on AMSR2 SWC data at Mongolia site was successfully removed using the brightness temperature (TB) data

## Slide 17
THANK YOU

## Slide 18: Data: Satellite data: Study area and data description
The study area is set to an area of 50 x 50 km that corresponding to the AMSR2 pixel of AMSR2 SWC (AMSR 2 Level 2 (L2) Soil Moisture Content (SMC) data products)..
Depending on the data quality and availability, the pixel that covers M1 area was selected for evaluation of the removal temperature effect method.
The in situ data are all averaged over the M1 area for comparison and evaluation.
The data period was chosen based on the longest data series. Since the data at C2 and A6 are not available from 1st Oct, 2015 to 4th Sep, 2016, the selected period for study ranges from 5th Sep, 2016 to 31st Oct, 2019.
Surface temperature product is also used.

## Slide 19: Data Assessment
When we analyzing the data first we have to eliminate the abnormal data (data that have drops or spikes)
To avoid the effects of precipitation because of the rainfall the days that have a daily rainfall amount larger than 0.1mm have been excluded
And also the days with negative soil temperature are excluded because the TDR calibration equation is not applicable to frozen soil

## Slide 20
Data: In situ data averaging - Thiessen Polygon Method
Precipitation, Soil Temperature,
Soil Water Content
recorded at various stations.
Area of Thiessen polygon
Number of stations
SWC
Spatially averaged data will be used.
SWC
Soil temperature

## Slide 21
Experimental facts about TE in TDR SWC measurement
Horizontal insertion
Vertical insertion
Volumetric SWC
Soil temperature
Notes: Experiments are carried out to confirm TE.
For glass beads of constant SWC, the sensor reading
Increase when temperature was raised.
Both horizontal and vertical insertion show TE.
Also our removal algorithm removed TE best.

## Slide 22: Study area and data description
Weighing index
Station name | Station ID | Network | Weighing
ASSH820 | C2 | ASSH | 0.204038
ASSH815 | C4 | ASSH | 0.158021
ASSH8122 | A3E | ASSH | 0.129942
ASSH817 | D1 | ASSH | 0.107943
ASSH813 | E4 | ASSH | 0.155352
ASSH819 | A6 | ASSH | 0.022081
ASSH811 | F2 | ASSH | 0.114076
MGS |  | AWS | 0.06894
DRS |  | AWS | 0.039608

## Slide 23: Existence of Temperature Effect (TE) in satellite Soil Water Content (SWC) data
Previous ascending
Following ascending
Areal mean of in-situ SWC, soil temperature, SMAP SWC at ascending and descending times and SMAP surface temperature at Oklahoma, USA (Hoang and Lu (2021))
Both ascending SWC are larger than descending SWC. Previous ascending SWC are larger than following ascending SWC (Hoang and Lu (2021)) .

## Slide 24: Study Area
Study area : Mongolia
Depending on the data quality and availability, the pixel that covers M1 area was selected for evaluation of the removal temperature effect method.
Annual rainfall 300mm-400mm
Land cover : forest, meadow steppe, real steppe, desert steppe, barren, sand, desert, ice, water, cropland and built area
Time in Mongolia is officially represented by the Mongolian Standard Time (UTC+08:00) However, the far western provinces of Khovd, Uvs and Bayan-Ölgii use UTC+07:00.
This study area is located between 45.75°N, 106.9°E and 46.2°N, 106.25°E

## Slide 25: Outliers
outlier is an extremely high or extremely low data point relative to the nearest data point and the rest of the neighboring co-existing values in a data graph or dataset
Methods of finding outliers
Sorting Datasheet to Find Outliers
Graphing Your Data to Identify Outliers (Boxplot, Histogram)
Using Z-scores to Detect Outliers
Finding Outliers with Hypothesis Tests
Studentized Residuals

## Slide 26: Studentized residual
To identify outliers, the preferred method is to use studentized residuals. For each data point i, the point is deleted and the regression model is re-estimated with the remaining data points. The residual of this data point is its Y-value minus the predicted Y-value from the regression. This is repeated for all the data points, and we are able to determine the standard deviation of the residuals.

## Slide 27: Automated temperature effects removal
High amplitude data points often distort the regression line by shifting it towards them, rainfall induced amplitude shifts need to be excluded from the process
SWC is influenced by rainfall events and therefore, and are as well. Hence, SWC data which correspond to rainfall events can be easily recognized.
In statistics, the data points which scattered away from major data cloud or unusually large or small values are referred to as high and low outliers, respectively. Statistical inference methods like confidence interval and statistical tests are widely used to identify such outliers
Many statisticians recommend using studentized residuals to detect outliers. Usually, the studentized residuals of a data set approximate a t-distribution with a known degree of freedom. By estimating the shifts from a required level of confidence in that t-distribution, outliers can be retrieved.
where and = observed and fitted amplitudes of SWC, respectively, = mean squared error of the regression fit calculated by removing observation and stands for the leverage value for observation
Firstly, a coefficient was estimated for the soil moisture data set (including rainy days) after filtering out the negative temperature days. Secondly, studentized residuals (Sri) were estimated by using Eq.
Subsequently, shifts of each studentized residual from the upper 99% confidence level of the studentized residuals t- distribution were evaluated. Afterwards, the data points which correspond to shifts larger than zero were removed as outliers.

## Slide 28: Application: Temperature effect removal
Applying newly developed method to in-situ data at ASC and DES time
A diagram of corrected SWC ASC and DES
Results and effects of temperature effect error removal for in-situ mimic data

## Slide 29: In-situ SWC data

## Slide 30: Radiative Transfer Model of the Soil Surface–Vegetation Layer
The low-frequency microwave radiative transfer used in soil moisture calculations is affected only slightly by the atmosphere. If these effects are ignored, the microwave brightness temperature of a land surface covered uniformly by vegetation, as observed by satellites, can be expressed as follows.
where the subscript 𝑝 represents the polarization of the waves; the subscript 𝑐 refers to a component related to the vegetation; is the microwave brightness temperature of the soil surface; and are the optical thickness and single scattering albedo of the vegetation layer, respectively; is the physical temperature of the vegetation; 𝛤 is the Fresnel power reflectivity; and 𝜃 is the incidence angle, which is fixed at 55 ° for the AMSR-E. The first term on the right-hand side of Eq. (1) represents the radiation from the ground surface dissipated by the vegetation layer; the second and third terms represent the upward radiation from the vegetation layer itself and the reflection of the downward radiation, respectively.
where is the soil physical temperature, 𝑄 is the polarization mixing ratio, ℎ′ is the roughness height, and 𝑞 is the opposite polarization from 𝑝. 𝑄 and ℎ′ are constants that depend on the surface roughness of the soil. Here, we define 𝐻=𝑒−ℎ′𝑐𝑜𝑠2𝜃. Values of 𝑄 and 𝐻 for each band (10 GHz and 36 GHz) can be determined by comparing the brightness temperature data observed by the AMSR-E with the in situ data at the Mongolia validation site

## Slide 31: Satellite SM data with TB