## Slide 1: An Analysis of the Use of Multiple Transmission Power Levels on Wireless Sensor Networks
Felipe Antonio Moura Miranda – Federal Institute of Education, Science and Technology of Sao Paulo
miranda@ifsp.edu.br
Paulo Cardieri – State University of Campinas
cardieri@decom.fee.unicamp.br

## Slide 2: Motivation
The energy consumption in wireless sensor networks is the critical concern of different studies, especially because of the great effort, or even the impossibility, to replace the battery of their motes.

## Slide 3: motivation
Consequently, it is fundamental to investigate and evaluate the energy spent by every individual task executed by the motes in order to provide an efficient use of their batteries.

## Slide 4: motivation
The contribution of this works is a detailed investigation of the impact caused by the use of different transmission power levels employing different metrics, offering a wide perspective on the subject.

## Slide 5: Introduction
The electronic industry is regularly lowering the power consumption of their products, achieving even figures of nanowatts.

## Slide 6: Introduction
The problem is that even a small, but continuous, consumption can deplete a battery, which usually is the primary power supply of a mote, in the long-term.

## Slide 7: Methodology
Simulations
  Model based on direct measurements
  Considers the different operational states
Common architecture:
  Battery: 150 mAh / 540 C
  Sensor: Texas Instruments LM75
  Transceiver: Digi Xbee PRO
  Microcontroller: Atmel Atmega8L
Battery
Transceiver
Sensor
Microcontroller

## Slide 8: Methodology
Transmission power levels
  Plane Earth Propagation Model : path loss exponent set to 3.5
  Reaching longer hops
    transmission power for reaching one hop
    transmission power for reaching two hops
    transmission power for reaching three hops
    transmission power for reaching four hops
    transmission power for reaching five hops
    transmission power for reaching, directly, the base station
Promiscuous reception was considered in all scenarios
  Unnecessarily received messages

## Slide 9: Transmission Power levels
Base Station
1
2
3
5
7
9
4
6
8
10
Transmitter: 10

## Slide 10: Transmission Power levels
Base Station
1
2
3
5
7
9
4
6
8
10
Transmitter: 10
Reach: 1 hop
Receivers: {9}
Addressee: 9

## Slide 11: Transmission Power levels
Base Station
1
2
3
5
7
9
4
6
8
10
Transmitter: 10
Reach: 3 hops
Receivers: {9,8,7}
Addressee: 7

## Slide 12: Transmission Power levels
Base Station
1
2
3
5
7
9
4
6
8
10
Transmitter: 10
Reach: 5 hops
Receivers: {9,8,7,6,5}
Addressee: 5

## Slide 13: Transmission Power levels
Base Station
1
2
3
5
7
9
4
6
8
10
Transmitter: 10
Reach: 10 hops
Receivers: {9,8,7,6,5,4,3,2,1}
Addressee: Base Station

## Slide 14: Transmission Power levels
Worse depending on the transmitter location

## Slide 15: Methodology
Network lifetime
  from the moment the network operation begins until the first mote runs out of battery
Network cost
  10 motes = U$445,10

## Slide 16: Methodology
Message log
  Listened Messages: All messages received by a mote, regardless their addressee.
  Rerouted Messages: All messages that a mote had to reroute in order to reach the base station.
  Overheard Messages: Only the messages that a mote received but were not addressed to it.
  Generated Messages: All messages created and transmitted by a mote.

## Slide 17: simulation
Simulated Network
  6 different traffic loads
Base Station
1
2
3
5
7
9
4
6
8
10

## Slide 18: Results
Primary Consumption
  Active states
    Transmission/reception
    Sensing, processing
Secondary Consumption
  Active states
    Transmission/reception
    Sensing, processing
Chart: Traffic Load (msg/s)
| 1.16E-05 | 2.78E-04 | 0.0016 | 0.016 | 0.1 | 1
1 hop | 0.0026 | 0.0598 | 0.2762 | 0.7925 | 0.9583 | 0.9958
2 hops | 0.0057 | 0.1209 | 0.4522 | 0.892 | 0.9803 | 0.9981
3 hops | 0.0123 | 0.2311 | 0.6433 | 0.9475 | 0.9909 | 0.9991
4 hops | 0.0222 | 0.3534 | 0.7663 | 0.9704 | 0.9949 | 0.9995
5 hops | 0.0356 | 0.4696 | 0.8416 | 0.9815 | 0.9968 | 0.9997
Max Ptx | 0.1189 | 0.7644 | 0.9511 | 0.9949 | 0.9991 | 0.9999

## Slide 19: Results
Transmission Power / Reach | Radio-Tx | Radio-Rx | Microcontroller | Sensor
1 hop | 32.03% | 24.70% | 41.18% | 2.08%
2 hops | 77.47% | 11.18% | 10.38% | 0.96%
3 hops | 91.11% | 4.96% | 3.48% | 0.44%
4 hops | 95.57% | 2.61% | 1.56% | 0.24%
5 hops | 97.52% | 1.52% | 0.80% | 0.15%
Base station | 99.47% | 0.34% | 0.14% | 0.04%
Energy consumption of each part/functionality
Increase

## Slide 20: Results
Radio | Microcontroller | Sensor
47.61% | 23.81% | 28.58%
Energy consumption profile of secondary states in all scenarios

## Slide 21: Results
Chart: Traffic Load (msg/s)
| 1.16E-05 | 2.78E-04 | 0.0016 | 0.016 | 0.1 | 1
1 hop | 7111.35 | 6457.86 | 4364.89 | 969.93 | 182.28 | 18.65
2 hops | 7067.55 | 5690.14 | 2821.47 | 437.78 | 76.89 | 7.76
3 hops | 6981.56 | 4595.49 | 1651.28 | 208.51 | 35.62 | 3.57
4 hops | 6863.59 | 3614 | 1041.33 | 119.86 | 20.26 | 2.1
5 hops | 6568.67 | 2307 | 526.16 | 56.35 | 9.45 | 0.94
Max Ptx | 4797.62 | 561 | 100 | 10.13 | 1.69 | 0.17
The difference between the lifetime of the simulated networks decreased when the traffic load got lower

## Slide 22: Results
The difference between the lifetime of the simulated networks decreased when the traffic load got lower
Chart: Traffic Load (msg/s)
2 hops | -0.0061592 | -0.11888 | -0.3536 | -0.54865 | -0.57818 | -0.58391
3 hops | -0.018251 | -0.28839 | -0.62169 | -0.78503 | -0.80459 | -0.80858
4 hops | -0.03484 | -0.44037 | -0.76143 | -0.87642 | -0.88885 | -0.8874
5 hops | -0.076312 | -0.64276 | -0.87946 | -0.9419 | -0.94816 | -0.9496
Max Ptx | -0.32536 | -0.91313 | -0.97709 | -0.98956 | -0.99073 | -0.99088

## Slide 23: Results
Traffic Load (msg/s) | Lifetime (in hours) – 1 hop | Lifetime (in hours) – 2 hops | Lifetime (in hours) – 3 hops | Lifetime (in hours) – 4 hops | Lifetime (in hours) – 5 hops | Lifetime (in hours) – Max Power
1.16E-05 | 7111.35 | 7067.55 | 6981.56 | 6863.59 | 6568.67 | 4797.62
2.78E-04 | 6457.86 | 5690.14 | 4595.49 | 3614.01 | 2307.02 | 561.01
0.00166 | 4364.89 | 2821.47 | 1651.28 | 1041.33 | 526.16 | 100.01
0.166 | 969.93 | 437.78 | 208.51 | 119.86 | 56.35 | 10.13
0.1 | 182.28 | 76.89 | 35.62 | 20.26 | 9.45 | 1.69
1 | 18.65 | 7.76 | 3.57 | 2.10 | 0.94 | 0.17
Lifetime of the simulated networks with different transmission powers.

## Slide 24: Results
All network costs per working got lower when the traffic generation was reduced
Chart: Traffic Load (msg/s)
| 1.16E-05 | 2.78E-04 | 0.0016 | 0.016 | 0.1 | 1
1 hop | 0.37 | 0.41 | 0.61 | 2.75 | 14.65 | 143.14
2 hops | 0.37 | 0.47 | 0.94 | 6.1 | 34.73 | 343.95
3 hops | 0.38 | 0.58 | 1.61 | 12.8 | 74.97 | 746.38
4 hops | 0.39 | 0.73 | 2.56 | 22.28 | 131.8 | 1314.48
5 hops | 0.4 | 1.15 | 5.07 | 47.4 | 282.42 | 2820.22
Max Ptx | 0.55 | 4.76 | 26.7 | 263.53 | 1581.01 | 15760.91

## Slide 25: results
Traffic Load (msg/s) | Network Cost per hour – 1 hop | Network Cost per hour – 2 hops | Network Cost per hour – 3 hops | Network Cost per hour – 4 hops | Network Cost per hour – 5 hops | Network Cost per hour – Max Power
1.16E-05 | US$0.06 | US$0.06 | US$0.06 | US$0.06 | US$0.07 | US$0.09
2.78E-04 | US$0.06 | US$0.07 | US$0.10 | US$0.12 | US$0.19 | US$0.79
0.00166 | US$0.10 | US$0.16 | US$0.27 | US$0.42 | US$0.84 | US$4.45
0.166 | US$0.46 | US$1.01 | US$2.13 | US$3.71 | US$7.90 | US$43.94
0.1 | US$2.44 | US$5.79 | US$12.49 | US$21.97 | US$47.10 | US$263.37
1 | US$23.86 | US$57.36 | US$124.68 | US$211.95 | US$473.51 | US$2,618.23
Network cost per hour of the simulated networks with different transmission powers

## Slide 26: Results
More power, less listened messages
Chart: Transmission Power Level
1 hop | 9.9
2 hops | 9.7
3 hops | 9.4
4 hops | 9
5 hops | 8.5
Max Ptx | 7

## Slide 27: Results
More power, less rerouted messages
Chart: Transmission Power Level
1 hop | 4.5
2 hops | 2
3 hops | 1.2
4 hops | 0.8
5 hops | 0.5
Max Ptx | 0

## Slide 28: Results
Overheard Messages: messages that a mote received but were not addressed to it.
  Increased, then decreased
Chart: Transmission Power Level
1 hop | 5.4
2 hops | 7.7
3 hops | 8.2
4 hops | 8.2
5 hops | 8
Max Ptx | 7

## Slide 29: Concluding remarks
The use of multiple transmission power levels achieved both positive and negative results, depending on the employed metric.
The results about the traffic of messages were very positive, but, it cannot be analyzed alone, without energy issues, due to the focus of this work on wireless sensor networks.
As the messages were sent further when using higher transmissions power levels, the quantity of rerouted messages also decreased. One result that can be inferred, but is not analyzed in this work, is that the less hops a message has to perform, the lower is the chance of it be corrupted or lost.

## Slide 30: Concluding remarks
The results indicate that the use of multiple transmission power levels would suit better in low message traffic networks or when dealing with reliability/message loss constraints.