## Slide 1
Ivan Gabriel-Martin, Alvaro Sordo-Ward, Luis Garrote & Isabel Granados
Departamento de Ingeniería Civil: Hidráulica, Energía y Medio Ambiente
NOVEMBER-2018
STOCHASTIC ASSESSMENT OF THE INFLUENCE OF RESERVOIR OPERATION IN HYDROLOGICAL DAM SAFETY THROUGH RISK INDEXES
3rd International Electronic Conference on Water Sciences (ECWS-3)

## Slide 2
Introduction
Introduction Materials and Methods Results and Discussion Conclusions
Failure of Large Dams is a concern in many countries.
Dam risk assesment has evolved lately. Importance of initial reservoir level.
Evolution of stochastic methodologies.
ECONOMIC ASSESMENT
PROPOSAL
STOCHASTIC METHODS
DAM AND DOWNSTREAM SAFETY
INITIAL RESERVOIR LEVEL

## Slide 3
Materials and Methods
Introduction Materials and Methods Results and Discussion Conclusions
Generation of synthetic inflow hydrographs.
Stochastic initial reservoir level assignation.
Reservoir-Dam system routing.
Risk-Index analysis.
Applied to a concrete gravity multipurpose dam
Reservoir Levels (m.a.s.l) |  | Maximum Outflow Capacity at Maximum Normal Level (MNL) (m3/s) | 
Maximum Normal Level (MNL) | 386 | Gated-spillway | 2200
Design flood level (DFL) | 387 |  | 
Crest of dam (COD) | 388 | Bottom outlet | 57

## Slide 4
Results and Discussion
Introduction Materials and Methods Results and Discussion Conclusions
Hydrograph generation
Damage Curves
Scenario 2 IR (103 euros)
980.5
Scenario 3 IR (103 euros)
93.0
Scenario 1 IR (103 euros)
1445.6
Initial Reservoir Level
Risk Index

## Slide 5
Conclusions
Introduction Materials and Methods Results and Discussion Conclusions
For the case study, considering the fluctuation of initial reservoir level provided a more realistic assessment of hydrological dam and downstream safety.
The global risk index reduced its value up to 93 % if variable initial reservoir level is accounted, from 1445.6 x103 to a value of 93.0 x103 euros in the case study.
The authors would like to thank the funds from Fundación José Entrecanales Ibarra in the framework of the Program “Support program for research purposes”. The authors acknowledge the computer resources and technical assistance provided by the Centro de Supercomputación y Visualización de Madrid (CeSViMa) and the funds from Universidad Politécnica de Madrid in the framework of their Program “Ayudas para contratos predoctorales para la realización del doctorado en sus escuelas, facultad, centro e institutos de I+D+i” and in the framework of their Program “Ayudas a dirigidas a jóvenes investigadores doctores para fortalecer sus planes de investigación”.
Acknowledgements
Sordo-Ward, A.; Gabriel-Martin, I.; Bianucci, P.; Garrote, L. A Parametric Flood Control Method for Dams with Gate-Controlled Spillways. Water 2017, 9, 237. https://doi.org/10.3390/w9040237
Main References
Gabriel-Martin, I.; Sordo-Ward, A.; Garrote, L.; G. Castillo, L. Influence of initial reservoir level and gate failure in dam safety analysis. Stochastic approach. J. Hydrol. 2017, 550, 669-684, https://doi.org/10.1016/j.jhydrol.2017.05.032