## Slide 1: Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics
Elisa Chiodi1, Allison M. Marn1, Matthew T. Geib1, Fulya Ekiz Kanik1, John Rejman2, David AnKrapp2, M. Selim Ünlü1,3
1 Boston University, dept. of Electrical Engineering, Boston (MA) USA
2 Neogen Corp., Lansing (MI) USA
3 Boston University, dept. of Biomedical Engineering, Boston (MA) USA

## Slide 2: Outline
The importance of small molecule characterization
Our approach: the Interferometric Reflectance Imaging Sensor (IRIS).
Beating the sensitivity limit: noise reduction methods and proof of concept experiments (Biotin, MW = 244Da).
Agro-biotech application: characterization of fumonisin B1 toxin (MW = 722 Da)
Conclusions and future work

## Slide 3: Outline
The importance of small molecule characterization
Our approach: the Interferometric Reflectance Imaging Sensor (IRIS).
Beating the sensitivity limit: noise reduction methods and proof of concept experiments (Biotin, MW = 244Da).
Agro-biotech application: characterization of fumonisin B1 toxin (MW = 722 Da)
Conclusions and future work

## Slide 4: Why small molecules?
Chart: 
| Proteins | Oligonucleotides | Others | Small molecules
Sales | 10 | 2 | 1 | 35
73% of 2019 FDA approved drugs1
99% of all toxins2
FDA approvals (2019)
73%
21%
4%
2%
[1] Mullard, Nature Reviews Drug Discovery 19, 79-84 (2020)
[2] Wishard, D. et al., T3DB: the toxic exposome database. Nucleic Acids Res. (2015)

## Slide 5: Why small molecules?
A small size implies…
Easy antibody-based recognition
Easy access to the cellular membrane

## Slide 6: Outline
The importance of small molecule characterization
Our approach: the Interferometric Reflectance Imaging Sensor (IRIS).
Beating the sensitivity limit: noise reduction methods and proof of concept experiments (Biotin, MW = 244Da).
Agro-biotech application: characterization of fumonisin B1 toxin (MW = 722 Da)
Conclusions and future work

## Slide 7: The IRIS system
t1
t2
Reflectance (A.U.)
Wavelength (nm)
[3] Daaboul, G.; Vedula, R.; Ahn, S.; Lopez, C.; Reddington, A.; Ozkumur, E.; Ünlü, M. LED-based Interferometric Reflectance Imaging Sensor for quantitative dynamic monitoring of biomolecular interactions. Biosens. Bioelectron. 2011, 26, 2221−2227.

## Slide 8: The IRIS system
2X objective
Beam splitter
Turn mirror
Camera
Integrating sphere
Chip holder fixture
XYZ stage
4-color LEDs
[3] Daaboul, G.; Vedula, R.; Ahn, S.; Lopez, C.; Reddington, A.; Ozkumur, E.; Ünlü, M. LED-based Interferometric Reflectance Imaging Sensor for quantitative dynamic monitoring of biomolecular interactions. Biosens. Bioelectron. 2011, 26, 2221−2227.

## Slide 9: Our approach: from printing to quantifying
[4] Chiodi, E.; Marn, A.M.; Geib, M.T.; Ekiz Kanik, F.; Rejman, J.; AnKrapp, D.; and Ünlü, M.S.; Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics ACS Omega 2020 5 (39), 25358-25364

## Slide 10: Outline
The importance of small molecule characterization
Our approach: the Interferometric Reflectance Imaging Sensor (IRIS).
Beating the sensitivity limit: noise reduction methods and proof of concept experiments (Biotin, MW = 244Da).
Agro-biotech application: characterization of fumonisin B1 toxin (MW = 722 Da)
Conclusions and future work

## Slide 11: Noise reduction: time and spatial averaging
AVERAGE
Time

## Slide 12: Noise reduction: time and spatial averaging

## Slide 13: Noise reduction: time and spatial averaging
AVERAGE
SNR = 30
SNR = 92.5

## Slide 14: Proof of concept: biotin detection (244 Da)
Time avg: 100 frames
Spatial avg: 50 spots
[4] Chiodi, E.; Marn, A.M.; Geib, M.T.; Ekiz Kanik, F.; Rejman, J.; AnKrapp, D.; and Ünlü, M.S.; Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics ACS Omega 2020 5 (39), 25358-25364

## Slide 15: Outline
The importance of small molecule characterization
Our approach: the Interferometric Reflectance Imaging Sensor (IRIS).
Beating the sensitivity limit: noise reduction methods and proof of concept experiments (Biotin, MW = 244Da).
Agro-biotech application: characterization of fumonisin B1 toxin (MW = 722 Da)
Conclusions and future work

## Slide 16: Fumonisin: characterization of a corn toxin
KLH1-10
CTx1-10
Neg.
Neg.
200 μm
440 spots, 20-plex chip
[4] Chiodi, E.; Marn, A.M.; Geib, M.T.; Ekiz Kanik, F.; Rejman, J.; AnKrapp, D.; and Ünlü, M.S.; Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics ACS Omega 2020 5 (39), 25358-25364

## Slide 17: Fumonisin: characterization of a corn toxin
[4] Chiodi, E.; Marn, A.M.; Geib, M.T.; Ekiz Kanik, F.; Rejman, J.; AnKrapp, D.; and Ünlü, M.S.; Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics ACS Omega 2020 5 (39), 25358-25364

## Slide 18: Fumonisin: characterization of a corn toxin
Antibody | kON (M-1s-1) | kOFF (10-4s-1) | KD(μM)
CT1 | 15.6 ± 2.2 | 6.82 ± 3.2 | 44 ± 22
CT2 | 11.0 ± 2.2 | 8.77 ± 4.4 | 80 ± 43
CT5 | 30.8 ± 2.7 | 5.13 ± 1.9 | 17 ± 6
CT8 | 20.0 ± 2.1 | 5.3 ± 2.1 | 27 ± 11
CT10 | 13.6 ± 2.7 | 3.9 ± 3.2 | 28 ± 24
KLH1 | 8.2 ± 1.5 | 17.9 ± 4.7 | 219 ± 70
KLH2 | 4.0 ± 0.7 | 15.2 ± 3.3 | 377 ± 103
KLH3 | 9.3 ± 1.1 | 14.1 ± 3.0 | 151 ± 37
KLH4 | 31.9 ± 5.7 | 21.5 ± 5.3 | 67 ± 22
[4] Chiodi, E.; Marn, A.M.; Geib, M.T.; Ekiz Kanik, F.; Rejman, J.; AnKrapp, D.; and Ünlü, M.S.; Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics ACS Omega 2020 5 (39), 25358-25364

## Slide 19: Outline
The importance of small molecule characterization
Our approach: the Interferometric Reflectance Imaging Sensor (IRIS).
Beating the sensitivity limit: noise reduction methods and proof of concept experiments (Biotin, MW = 244Da).
Agro-biotech application: characterization of fumonisin B1 toxin (MW = 722 Da)
Conclusions and future work

## Slide 20: Conclusions and future work
The IRIS approach to small molecule characterization is…
  Highly sensitive
  Versatile and multiplexable
  Label-free
Sensitivity can improve from current 1pg/mm2 to 0.2pg/mm2 thanks to a novel camera sensor
Bulk effect reduction methods: further reduction of noise

## Slide 21: Conclusions and future work
[4] Chiodi, E.; Marn, A.M.; Geib, M.T.; Ekiz Kanik, F.; Rejman, J.; AnKrapp, D.; and Ünlü, M.S.; Highly Multiplexed Label-Free Imaging Sensor for Accurate Quantification of Small-Molecule Binding Kinetics ACS Omega 2020 5 (39), 25358-25364

## Slide 22: Thank you!
Prof. Selim Ünlü
Allison M. Marn
Matthew T. Geib
Fulya Ekiz Kanik
David AnKrapp (Neogen, Corp.)
John Rejman (Neogen, Corp.)
Iris Celebi
Negin Zaraee
Celalettin Yurdakul

## Slide 23: Any questions?
Elisa Chiodi
Ph.D. Candidate – OCN Laboratory @ Boston University
elich@bu.edu