## Slide 1
One hour in vivo-like phenotypic screening system
for anti-cancer drugs
using a high precision surface Plasmon resonance device
Junko Johzuka 1,2,*, and Toshihiro Ona 2,1
1 O'Atari Inc., Onojo, Fukuoka, Japan.
2 Graduate School of Bioresource and Bioenvironmental Sciences, Kyushu University, Fukuoka, Fukuoka, Japan.
* Corresponding author: info@oatari-inc.com

## Slide 2
Graphical Abstract
One hour in vivo-like phenotypic screening system
for anti-cancer drugs using a high precision surface Plasmon resonance device

## Slide 3
Abstract: In anti-cancer drug (candidate) screening, the demand exists for evaluation at physiological concentrations similar to in vivo. This is often performed by 3D cultured cells. It necessitates a long culture period of 2-4 weeks with tedious experimental procedures based on endpoint assay and labeling agents causing low reliability. The previous device methods depend on the pharmaceutical mode of action, little related to the conventional method. Furthermore, a separate set of experiment is required to obtain both efficacy and toxicity. Here, we report on a high precision surface Plasmon resonance-3D system to overcome these all problems sensing dynamic cellular reaction against target compound(s) by laser. We developed the system with average fluctuation of 50 ndeg/s combined with 2D cultured cells attached onto a sensor chip by applying collagen on the top. The 3D cell activity was shortly obtained by this without cell division. New system gave real-time monitoring of mitochondrial membrane potential (MMP) within live cells without both labeling and invasion. It allowed in vivo-like phenotypic screening for anti-cancer drugs within 1h of drug addition. The data were collected as the stable linear signal change parts for at least 5min after 25min following drug addition. The results provided compatibility to clinically related chemosensitivity test (P<0.001) using two cell lines of pancreatic cancer and three anti-cancer drugs to represent differences in individual gene expression and drug mode of action. Early MMP change rate is concluded as a key to quantitatively predict the efficacy and toxicity.
Keywords: phenotypic; screening; cancer; device; in vivo-like

## Slide 4
Introduction
Steps for efficacy and toxicity prediction of
bioactive compounds
In vitro cell-based test
Animal test
Clinical test
Rapid and reliable in vitro cell-based test is demanded
for discovery of bioactive compounds
Key is efficacy and toxicity prediction technology
extremely before endpoint of test!
Animal test should be avoided based on opinions.

## Slide 5
Introduction: Conventional method – Cocultivation method
Cocultivation method（Cell-based assay）
Measurement of traits such as cell viability by fluorescence stain and microscope or flow cytometer after 7-30 days of cocultivation of target compounds with live cells embedded in extra cellular matrix such as collagen (3D cell culture)

## Slide 6
Introduction: Advantage & disadvantage of 3D cell culture
3D cell culture with extra cellular matrix
---Reproduction of in vivo cell condition
---Long decision duration with medium exchange (~30days)--- Slow---
Large test error--- Low reliability
---Standard method---High reliability
---Independent to compound mode of action and to personal difference
--- High reliability
Label requirement---Large test error---Low reliability
Difficulty in evaluation of efficacy and toxicity with one experimental set-up--- Low reliability
Complicated handling---Laboring + Automation shortage---Slow
Many cells required (106) ---Difficulty in applying to tumors
Rapid, in vivo-like label-free cell-based assay is demanded
Cocultivation method（Cell-based assay）

## Slide 7
Introduction: Commercialized devices
Commercialized devices （Microphysiometer etc）
Measurement of cellular statuses such as extracellular fluxes of H+, O2, and cell morphology changes using impedance and semiconductor during 1-4 days of cocultivation of target compounds with live cells

## Slide 8
Introduction: Disadvantege of commercialized devices
Commercialized devices （Microphysiometer etc）
Disadvantage
Medium exchange
Long decision duration-half of endpoint
Cause of artifact on live cells by impedance etc
Large test error
Low reliability in polypharmacy
Difference from physiological concentration
Low compatibility with chemosensitivity test
Rapid, in vivo-like label-free and non-invasive cell-based assay is demanded

## Slide 9
Introduction: Original technology – HP-SPR
High Precision-Surface Plasmon Resonance (HP-SPR)
− One of laser spectroscopic methods with non-label and real-time analysis to detect refractive index change derived from interaction between molecules etc. −
Detection of live cell reaction − Apply to efficacy prediction of target compounds −
ca 50 nm gold film
10K to 1M times higher sensitivity compared
to commercial instrument !
Temp. control
Low vibration
Algorithm
Beam mold
Chip design
Cell reaction = dielectric constant of a few 100 n/s

## Slide 10
Introduction: Original technology – HP-SPR
HP-SPR
q
Cell dielectric constant (polarization) change can be detected by SPR sensor
Mitochondrial membrane potential (MMP) change by simultaneous fluorescence microscopy using specific inhibitors

## Slide 11
Introduction: Original technology – HP-SPR-2D
HP-SPR-2D
Breakthrough
Early mitochondrial polarization change rate after addition of a target compound is a key to quantitatively predict the final compound efficacy against live cells!

## Slide 12
Objectives
The HP-SPR-2D system uses 2D cells attached onto a sensor chip, which does not allow anti-cancer drug evaluation at physiological concentrations. Theoretically, SPR can detect only materials attached or very close at nearly half of incident light wavelength. Consequently, we cannot use 3D cultured cells for the HP-SPR system.
Here, we report on the newly proposed HP-SPR-3D system, which evaluates the efficacy of an anti-pancreatic cancer drug at physiological concentrations. Because pancreatic cancer does not respond to many anti-cancer drugs efficiently contrary to other types of cancer, the number of deaths is increasing in pancreatic cancer patients. Thus, our first target focused on pancreatic cancer.
First, HP-SPR-3D was examined by the activation of 2D cells into in vivo-like status on a sensor chip without cell division by applying collagen on the top of the cells.
Second, the HP-SPR-3D results obtained were compared to the results of a clinically related chemosensitivity test for pancreatic cancer, collagen droplet embedded culture drug sensitivity test (CD-DST), and the HP-SPR-3D was validated as an in vivo-like system.

## Slide 13
Results and discussion: Schematic diagram of HP-SPR-3D

## Slide 14
Results and discussion: SPR angle trend in MIA PaCa-2 cancer cells with 2D and 3D conditioned status exposed to 50nM doxorubicin

## Slide 15
Results and discussion: Change rate in SPR angle in MIA PaCa-2 cancer cells with incubation duration with collagen exposed to 50nM doxorubicin

## Slide 16
Results and discussion: Relationship between cell viability by CD-DST and Change rate in SPR angle exposed to various concentrations of drugs (Error bar shows SEM)

## Slide 17
Breakthrough
3D cell activity is obtained by conditioning of 2D attached cells covered by extra cellular matrix for short time with no cell division !
Breakthrough
Early mitochondrial polarization change rate after compound addition is a key to quantitatively predict the final efficacy and toxicity properties!
Breakthrough
Custom-made instrument with 10K to 1M times higher sensitivity compared to commercial one.
HP-SPR-3D
Conclusions

## Slide 18
Potential application for HP-SPR-3D

## Slide 19
References
Kosaihira, A. and Ona, T. Rapid and quantitative method for evaluating the personal therapeutic potential of cancer drugs. Analytical and Bioanalytical Chemistry, Vol. 391 (5): 1889-1897 (2008).
Ona, T. and Shibata, J. Advanced dynamic monitoring of cellular status using label-free and non-invasive cell-based sensing technology for the prediction of anti-cancer drug efficacy. Analytical and Bioanalytical Chemistry, Vol. 398 (6): 2505-2533 (2010).
Johzuka, J., Ona, T. and Nomura, M. One Hour in vivo-like phenotypic screening system for anti-cancer drugs using a high precision surface plasmon resonance device. Analytical Sciences, Vol. 34 (10): 1189-1194 (2018).

## Slide 20
Acknowledgments
This research was supported by O’Atari Inc., Kyushu University and a grant from the Regional Research and Development Resources Utilization Program of the Japan Science and Technology Agency (JST).
O’Atari Inc.