## Slide 1
MICROWAVE-ASSISTED CONTINUOUS FLOW FOR THE SELECTIVE OLIGOMERIZATION OF GLYCEROL
Remi Nguyen, Nicolas Galy, Christophe Len
christophe.len@chimieparistech.psl.eu
1st Int. Elect. Conf. Catal. Sci., November 2020,
@len_research
lenresearch.com

## Slide 2
1st Int. Elect. Conf. Catal. Sci., November 2020,
Notes: @

## Slide 3
WHAT ARE THE TOOLS & LEVERS ?
BENIGN BY DESIGN PROCESSES & TECHNOLOGIES
In term of the processes & technologies
Homogeneous catalysis & Heterogeneous catalysis from bio-based derivatives or not
Nanocatalysis
Micellar catalysis
CATALYSIS
Continuous flow
Microwave irradiation in batch & in continuous flow
Ultrasound activation in batch & in continuous flow
Sunlight / UV in batch & in continuous flow
Electrochemistry in batch & in continuous flow
Ball Milling in batch & in continuous flow
ALTERNATIVE ENERGY SOURCES
Supercritical fluid (CO2, MeOH, CH3CN, H2O…)
Ionic Liquids
Water
Polyethyleneglycol (PEG)
Solvent free « Best solvent is no solvent »
ALTERNATIVE REACTION MEDIA
Low amount of catalyst
Bio-inspired catalyst
Room temp reaction
Eco-friendly solvents

## Slide 4
CONT. CHEMICAL PRODUCTION – A PARADIGM SHIFT
Current methods of synthesis for pharmaceuticals (APIs) and fine chemicals are entirely based on traditional batch manufacturing protocols.
Batch protocols have severe limitations compared to continuous flow processing.
Slow temperature control
Inefficient mass and heat transfer
Dangerous temperature gradients
Safety issues for many transformation
Instantaneous heating/cooling
Very fast mixing (<1s)
No concentration/temperature gradients
Inherently safe
Segmented individual steps
Processing a specific quantity
Multi purpose equipment
Quality managed by repetition and testing
Integrated synchronized operations
Continuous flow of product
Equipment dedicated for purpose
Quality managed by design and processes control of steady state
Lower cost level (operational, invest)
Increased productivity (small plant, low hold-up)
Shorter throughput time (less inventory)
Consistent quality (less off-spec, less by-products)

## Slide 5
VALUE ADDED CHEMICALS
ALTER. TECHNOL.
Lignocellulose
Carbohydrate
Oil
critical fluids
vs
Microwave / Ultrasound
enzyme
Petrol
Ball milling
STARTING MATERIALS
Vis
Green Solvent
critical fluids
vs
Microwave / Ultrasound
enzyme
Ball milling
Vis
Green Solvent
OUR EXPERTISES
1st Int. Elect. Conf. Catal. Sci., November 2020,

## Slide 6
Chart: Years
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 | 1872 | 2017 | 2159 | 2170 | 2460 | 2427 | 2697 | 2826 | 3120 | 3449 | 3675 | 4184 | 4381 | 4494 | 4711 | 4549 | 4632 | 4723 | 4834 | 5001 | 3708 | 16
« Glycerol »
in article title, abstract, keywords
from 2000 to present, 74,116 publications
HIKE AROUND GLYCEROL
1st Int. Elect. Conf. Catal. Sci., November 2020,

## Slide 7
Chart: Years
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 | 1872 | 2017 | 2159 | 2170 | 2460 | 2427 | 2697 | 2826 | 3120 | 3449 | 3675 | 4184 | 4381 | 4494 | 4711 | 4549 | 4632 | 4723 | 4834 | 5001 | 3708 | 16
« Glycerol »
in article title, abstract, keywords
from 2000 to present, 74,116 publications
Chart: Years
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
 | 41 | 66 | 44 | 68 | 55 | 83 | 90 | 130 | 209 | 251 | 265 | 312 | 324 | 281 | 240 | 240 | 247 | 180 | 182 | 233 | 120
« Glycerol »
in patent
from 2000 to present, 3,661 patents
HIKE AROUND GLYCEROL
1st Int. Elect. Conf. Catal. Sci., November 2020,

## Slide 8
VEGETABLE OIL
RAPESEED
SUNFLOWER
BLEND WITH DIESEL
(10 Tons)
CH3OH
(1 Tons)
(10 Tons)
BIODIESEL
(1.2 Ton)
Price: 270 €/Ton
GLYCERIN
GLYCEROL
(1 Ton)
Price: 550 €/Ton
Energy
consuming
process !
Sustainable Chem. Process. 2014, 2,1; J. Chem. Technol. Biotechnol. 2017, 92, 14; Energy Convers. Manage. 2017, 149, 355; Synthesis, 2018, 50, 723; Curr. Opin. Green Sustain. Chem. 2019, 15, 83.
HIKE AROUND GLYCEROL

## Slide 9
Sustainable Chem. Process. 2014, 2,1; J. Chem. Technol. Biotechnol. 2017, 92, 14; Energy Convers. Manage. 2017, 149, 355; Synthesis, 2018, 50, 723; Curr. Opin. Green Sustain. Chem. 2019, 15, 83.
HIKE AROUND GLYCEROL
✓

## Slide 10
POLYGLYCEROL
INDUSTRIAL APPLICATIONS OF POLYGLYCEROLS
Triglycerol
Glycerol
Diglycerol
Tetraglycerol
Esters of polyglycerol for incorporation
in food as an emulsifier
in polymers as antifogging and antistatic agents, or lubricants
in inks and agrochemical formulations as emulsifiers, stabilizers, dispersants or humectants
in the paper and wastewater industries as antifoaming agents …
Polyglycerols for incorporation
in polymers as plasticizer
as ink ingredients
in polyurethane production.
Molecules 2016, 21, 1038; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts 2017, 7, 123; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts. 2017, 7, 123.

## Slide 11
POLYGLYCEROL
INDUSTRIAL APPLICATIONS OF POLYGLYCEROLS
Triglycerol
Glycerol
Diglycerol
Tetraglycerol
Molecules 2016, 21, 1038; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts 2017, 7, 123; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts. 2017, 7, 123.
Polyglycerol esters of fatty acids (PGEs) are used in food as an emulsifier, allowing water and flour to mix.
Influence of PGPR addition (0.2%) to a molten chocolate (27% cocoa butter)
Castor bean plant
Ricinus communis
PGPR (E476)

## Slide 12
ISOMERS PG2 AND PG3 AND CYCLIC ISOMERS cPG2
POLYGLYCEROL

## Slide 13
LINEAR/BRANCHED ISOMERS PG2 AND PG3
POLYGLYCEROL
Molecules 2016, 21, 1038; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts 2017, 7, 123; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts. 2017, 7, 123.
Dehydration
Dehydration

## Slide 14
MW-ASSISTED CONT. GLYCEROL OLIGOMERIZATION
Water-free reaction
Molecules 2016, 21, 1038; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts 2017, 7, 123; J. Ind. Eng. Chem. 2017, 51, 312; Catalysts. 2017, 7, 123.
Company’s specifications
Cheapest possible catalyst that gives
the best possible result.
Not working on 1 mg of glycerol but on more than 200 g of glycerol.
GLYCEROL 240 g

## Slide 15
Water-free reaction
Entry | Flow | Res. Time | Composition (wt%) of the product by GC |  |  |  | 
 | (mL min-1) | (min) | PG1 | PG2 | PG3 | PG4 | other
1 | 1.0 | 20 | 84.0 | 12.1 | 2.4 | 0.2 | O.4
2 | 0.5 | 40 | 70.3 | 19.5 | 6.3 | 1.0 | 2.0
3 | 0.25 | 80 | 59.1 | 22.1 | 9.3 | 4.4 | 5.0
Reaction conditions: glycerol (240 g, 2.61 mol), K2CO3 (10.0 g, 72.4 mmol), 238 °C.
MW-ASSISTED CONT. GLYCEROL OLIGOMERIZATION

## Slide 16
Water-free reaction
Entry | Time | Composition (wt%) of the product by GC |  |  |  | 
 | (min) | PG1 | PG2 | PG3 | PG4 | other
1 | 50 | 85.9 | 12.3 | 1.5 | 0.2 | 0.1
2 | 100 | 71.8 | 20.6 | 5.2 | 1.2 | 1.2
3 | 150 | 62.1 | 25.5 | 7.9 | 2.3 | 2.2
4 | 250 | 55.1 | 26.4 | 10.0 | 3.7 | 4.8
5 | 250 | 55.2 | 24.2 | 9.2 | 3.4 | 7.4
Reaction conditions: glycerol (240 g, 2.61 mol), K2CO3 (10.0 g, 72.4 mmol), 238 °C,
0.5 mL min-1.
To achieve higher conversion, our system has been transformed to work in cycle by continuously reinjecting the output in the reactor
MW-ASSISTED CONT. GLYCEROL OLIGOMERIZATION

## Slide 17
Reaction conditions: glycerol (240 g, 2.61 mol), K2CO3 (10.0 g, 72.4 mmol), 238 °C, 250 min,
0.5 mL min-1.
Chart: PG2
| 100 | 200 | 300 | 400
 | 73.9 | 73.2 | 72.4 | 71.5
 | 24.9 | 25.6 | 26.3 | 27.1
 | 1.1 | 1.2 | 1.3 | 1.4
a,a-diglycerol selectivity 72-74%
a,b-diglycerol selectivity 25-27%
b,b-diglycerol selectivity 1%
Chart: PG3
| 100 | 200 | 300 | 400
 | 46.4 | 46.1 | 45.7 | 44.9
 | 45.4 | 45.2 | 45.3 | 45.7
 | 5.3 | 5.7 | 5.9 | 6.2
 | 2.5 | 2.7 | 2.7 | 2.9
 | 0.3 | 0.4 | 0.3 | 0.4
a,a-a,a-triglycerol selectivity 45% a,a-a,b-triglycerol selectivity
a,a-b,a-triglycerol selectivity
Others less than 6%
45%
MW-ASSISTED CONT. GLYCEROL OLIGOMERIZATION

## Slide 18
Entry | Fraction | Composition (wt%) of the product by GC |  |  |  |  |  |  |  | 
 |  | PG1 | cPG2 | PG2 | cPG3 | PG3 | PG4 | PG5 | PG6 | other
1 | Crude | 55.2 | 1.6 | 24.2 | 0.7 | 9.2 | 3.4 | 1.5 | 0.6 | 3.0
2 a | Distillat | 90 | 2.2 | 6.3 | 0.2 | 0.5 | - | - | - | 0.8
3 a | Residue | - | - | 50.2 | 2.0 | 22.1 | 9.5 | 4.3 | 2.0 | 7.4
In order to obtain a sample of oligomers with no glycerol or less amount of glycerol, short path evaporation has been explored.
a Short path evaporation: 0.1 mbar and 150°C.
Reaction conditions: glycerol (240 g, 2.61 mol), K2CO3 (10.0 g, 72.4 mmol), 238 °C, 250 min,
0.5 mL min-1.
Furthermore the purification removed PG1, cPG2, a more lipophylic byproduct and PG2
and a 50% enriched dimer mixture is obtained.
MW-ASSISTED CONT. GLYCEROL OLIGOMERIZATION

## Slide 19
CONCLUSION AND PERSPECTIVES
(1.2 Ton)
Price: 270 €/Ton (2017)
(1 Ton)
Price: 550 €/Ton (2017)
Price: 1324 €/Ton (<2000)
Due to a substantial decrease in the price of purified glycerol between 2000 and today, the purification of glycerin is getting less attractive.
Therefore, direct use of crude glycerol (or glycerin) is becoming promising as well as the transformation of Used Cooking Oil
Starting from Used Cooking Oil and Glycerin, chemical production can be manufactured with low price and sustainable supply.
GLYCERIN
GLYCEROL
Energy
consuming
process !
Mol. Catal. 2020, 494, 111128.

## Slide 20
CONCLUSION AND PERSPECTIVES
Lignocellulose
Carbohydrate
Oil
Petrol
Continuous Flow and Catalysis
Continuous Flow + MW
Continuous Flow + US
Continuous Flow + hn
Continuous Flow + Ball Milling

## Slide 21
MICROWAVE-ASSISTED CONTINUOUS FLOW FOR THE SELECTIVE OLIGOMERIZATION OF GLYCEROL
Remi Nguyen, Christophe Len
christophe.len@chimieparistech.psl.eu
@len_research
lenresearch.com
1st Int. Elect. Conf. Catal. Sci., November 2020,