## Slide 1: A QGIS based workflow for optimized cable road layout planning
#2 Identifying support and anchor trees from remote sensing data
Objective: Predicting Tree Height and DBH from available Remote Sensing data
72 method combinations were evaluated (3 Types of CHM x 8 Filter Methods x 3 Tree detection algorithms)
Best results were achieved based on ALS Data - resolution dependent Gauss Filter - local maxima tree detection algorithm
Tree position and tree height of the correctly detected trees show useful accuracies for cable line planning.
Fig.: Result of a single tree detection
Inventory
Detected
Canopy
Height Model
#3 Manual
Editing
#1 Optimize cable road layout
[II]
Decisions:
Locate Intermediate Supports
Location?
Height?
[I]
α
[III]
Load Path
Standing Skyline [Catenary]
Objective: Minimize number and height of intermediate supports
[Bont and Heinimann 2012]
Context: Cable logging is the principal wood extraction method in steep terrain.
Planning of a cable road is a complex task
Available planning tools do not fulfil the requirements of the practice (unprecise or unknown method to compute skyline properties / not integrated in a GIS / do not optimize the solution)
Solution may not be feasible as not matched with existing trees (for supports)
Results: Workflow in QGIS
L. Bont, L. Ramstein, F. Frutig, P. Moll, H. Heinimann and J. Schweier Swiss Federal Institute for Forest, Snow and Landscape Research / ETH Zurich Contact: leo.bont@wsl.ch 1st International Electronic Conference on Forests, 15–30 November 2020
#3 Manual editing
Geodata (DEM, Start & Endpoint)
Mechanical Properties Cable Road
Optimized theoretical solution
Feasible solution
#2 Support trees
#1 Layout Optimization
Download available on github:
piMoll/SEILAPLAN
?
Aim: User friendly QGIS plugin, containing an optimization algorithm based on catenary and detecting support trees
WHFF-CH
Conclusions & Outlook: Workflow simplifies Cable Road planning and calculates more efficient solutions
Master version available
Ability for manual editing remains necessary
Constraints:
[I] Stresses & strains within limits
[II] Min. clearance
[III] Min. gradient