## Slide 1: Influence of Ponsse Gazzelle forwarder passes on the soil environment and soil deformation
Msc eng. Dariusz Pszenny Warsaw University of Life Sciences Faculty of forestry, Forest Utilisation department

## Slide 2: Aim of the study
Determination of the:
Soil condition of the felling area through measurements during and after the cutting and skidding of wood.
Soil moisture and penetration ressistance changes.
% of soil damage over cut area.
Assesing of rut depth by using UAV photgrammetry and software.

## Slide 3: Area of research
Gidle Forest district

## Slide 4: Material and methods

## Slide 5: The research was conducted in two stages
Stage one:
Measurements with hand penetrometer
Taking soil samples for examining moisture
UAV flight for data registration
Stage two:
Creation of orthomosaics and digital elevation models using Agisoft metashape software

## Slide 6: Material and methods

## Slide 7: Material and methods

## Slide 8: UAV & flight parameters
DJI Phantom 4 Advanced
20 Mpx camera witch 1 inch CMOS sensor
Photos in 5472x3078 pixels resolution
Flight on 30 meters altitude
Photos overlap indicator 80% (both horizontal and vertical)

## Slide 9: Material and methods

## Slide 10: The research covered 4 harvesting sites

## Slide 11: Sites specification
Site nr | Habitat type | Site moisture | Soil type
1 | BMW | ++++ | Bgms
2 | BW | +++ | Bgts
3 | BMŚw | ++ | RDB
4 | BŚW | + | Bw
Bśw – fresh coniferous; Bw – moist coniferous; BMśw – fresh mixed coniferous; BMw – moist mixed coniferous.
Bw – podzolic soil Bgms, Bgts – glial-podzolic soil, RDb – rusty podzolic soil

## Slide 12: Soil penetration ressistance
Chart: Number of forwarder passes
L10 | 1.1355 | 1.2548 | 1.2968 | 1.4 | 1.5097 | 1.5258 | 1.5419 | 1.5677 | 1.6871 | 1.7452 | 1.871 | 1.9806 | 2.1194 | 2.2903 | 2.4613 | 2.6129 | 2.7968 | 3.0516 | 3.5161 | 3.5258 | 3.8742
R10 | 1.1839 | 1.2742 | 1.3097 | 1.3452 | 1.4355 | 1.4613 | 1.5419 | 1.6323 | 1.7 | 1.8581 | 1.8935 | 1.9258 | 2.0871 | 2.1613 | 2.3903 | 2.5097 | 2.8323 | 3.0065 | 3.3806 | 3.4194 | 3.9
M10 | 0.91613 | 0.99032 | 1 | 1.0065 | 1.0097 | 1.1581 | 1.1871 | 1.1871 | 1.3 | 1.3871 | 1.4194 | 1.429 | 1.4871 | 1.4935 | 1.5516 | 1.6 | 1.629 | 1.6548 | 1.7516 | 1.8613 | 1.8742
L20 | 1.4839 | 1.6613 | 1.6968 | 1.7194 | 1.9968 | 2.1032 | 2.1194 | 2.1806 | 2.2161 | 2.4516 | 2.8065 | 2.9065 | 3.1323 | 3.471 | 3.7419 | 4.0323 | 4.3613 | 4.9 | 5.4903 | 5.771 | 6.3258
R20 | 1.4516 | 1.6516 | 1.6677 | 1.7258 | 1.9871 | 2.0581 | 2.0613 | 2.3516 | 2.3871 | 2.4548 | 2.6516 | 2.8323 | 3.0419 | 3.2645 | 3.6129 | 3.8548 | 4.329 | 4.7387 | 5.5129 | 5.5903 | 6.2742
M20 | 1.1839 | 1.1968 | 1.3806 | 1.3935 | 1.3968 | 1.5903 | 1.6032 | 1.7968 | 1.8387 | 1.9516 | 2.0484 | 2.0516 | 2.2355 | 2.271 | 2.2742 | 2.3484 | 2.4387 | 2.6032 | 2.9161 | 3.0968 | 3.2452

## Slide 13: Soil penetration ressistance changes
Transect | Placement | Number of passes |  |  |  |  |  | Mean % soil compactness increase after single pass
 |  | 0 | 1 | 5 | 10 | 15 | 20 | 
1 | left rut | 1,25 | 1,85 | 2,43 | 3,17 | 3,42 | 4,29 | 6,70%
2 | left rut | 1,05 | 1,29 | 1,78 | 2,60 | 3,04 | 4,42 | 7,80%
3 | left rut | 1,48 | 1,72 | 2,14 | 2,90 | 4,00 | 6,24 | 6,40%
4 | left rut | 1,25 | 1,85 | 2,43 | 3,17 | 3,42 | 4,29 | 6,70%
1 | middle | 1,00 | 1,49 | 1,77 | 1,89 | 2,00 | 2,08 | 3,90%
2 | middle | 1,04 | 1,07 | 1,45 | 1,75 | 1,87 | 2,45 | 4,60%
3 | middle | 1,20 | 1,18 | 1,60 | 1,96 | 2,28 | 3,29 | 8,48%
4 | middle | 1,00 | 1,49 | 1,77 | 1,89 | 2,00 | 2,08 | 3,90%
1 | right rut | 1,31 | 1,87 | 2,41 | 3,20 | 3,57 | 4,27 | 6,40%
2 | right rut | 1,29 | 1,37 | 1,78 | 2,61 | 2,99 | 4,07 | 6,20%
3 | right rut | 1,45 | 1,66 | 1,96 | 2,81 | 3,84 | 6,27 | 6,63%
4 | right rut | 1,31 | 1,87 | 2,41 | 3,20 | 3,57 | 4,27 | 6,40%
Transect | Placement | Number of passes |  |  |  |  |  | Mean % soil compactness increase after single pass
 |  | 0 | 1 | 5 | 10 | 15 | 20 | 
1 | left rut | 1,66 | 2,52 | 3,41 | 4,97 | 5,38 | 6,40 | 7,40%
2 | left rut | 1,23 | 1,64 | 2,44 | 3,58 | 4,49 | 6,06 | 8,70%
3 | left rut | 1,14 | 1,40 | 1,54 | 1,98 | 2,61 | 3,87 | 8,74%
4 | left rut | 1,66 | 2,52 | 3,41 | 4,97 | 5,38 | 6,40 | 7,40%
1 | middle | 1,39 | 2,16 | 2,39 | 2,72 | 2,92 | 3,06 | 4,20%
2 | middle | 1,27 | 1,39 | 1,93 | 2,32 | 2,62 | 3,61 | 5,60%
3 | middle | 0,92 | 1,01 | 1,16 | 1,30 | 1,49 | 1,87 | 4,77%
4 | middle | 1,39 | 2,16 | 2,39 | 2,72 | 2,92 | 3,06 | 4,20%
1 | right rut | 1,73 | 2,44 | 3,32 | 4,90 | 5,91 | 7,08 | 7,70%
2 | right rut | 1,48 | 1,74 | 2,47 | 3,69 | 4,36 | 5,84 | 7,50%
3 | right rut | 1,18 | 1,35 | 1,46 | 1,89 | 2,51 | 3,90 | 6,83%
4 | right rut | 1,73 | 2,44 | 3,32 | 4,90 | 5,91 | 7,08 | 7,70%
10 cm
20 cm

## Slide 14: Soil density changes before & after 20 forwarder passes
Placement | Depth | Transect |  |  | 
 |  | 1 | 2 | 3 | 4
Left Rut | 10 cm | 341.9% | 418.7% | 422,3% | 341.9%
Middle |  | 208.4% | 235.6% | 273,9% | 208.4%
Right Rut |  | 325.9% | 316.0% | 431,4% | 325.9%
Left Rut | 20 cm | 385.4% | 491.9% | 341,2% | 362.7%
Middle |  | 410.5% | 394.3% | 204,6% | 394,3%
Right Rut |  | 219.7% | 283.0% | 329,4% | 313.4%

## Slide 15: Moisture changes
 | Transect |  |  | 
Placement | 1 | 2 | 3 | 4
Measure outside skid track (refrence) | 42,2% | 15,5% | 13,7% | 14,9%
Skid track before forwarder passes | 37,3% | 9,0% | 8,6% | 6,0%
Skid track after 20 forwarder passes | 14,6% | 5,8% | 5,8% | 3,9%

## Slide 16: UAV based data

## Slide 17: Site coverage
Site | 1 | 2 | 3 | 4
Area declared to cut | 1,21 | 1,29 | 1,84 | 1,91
Area measured after cut | 1,35 | 1,23 | 1,75 | 2,04
Difference [Ha] | 0,14 | -0,06 | -0,09 | 0,13
Difference % | 11,13% | -4,56% | -4,66% | 6,70%
Skid trails lenght [km] | 1,35 | 1,23 | 1,69 | 1,38
Skid trails per 1 Ha | 1,00 | 1,00 | 0,97 | 0,67
Skid trails area [ha] | 0,41 | 0,38 | 0,42 | 0,52
% of cut area covered with skid trails | 33,72% | 29,23% | 21,85% | 28,05%
Area with soil damage to the mineral layer [Ha] | 0,053 | 0,007 | 0,05 | 0,055
Converted to % share in the area of the trails area | 10,13% | 1,50% | 7,81% | 10,24%
Converted to % share of measured cut area | 3,92% | 0,57% | 2,85% | 2,70%

## Slide 18: Wheel rut depth

## Slide 19: Rut depth
Site nr | Habitat type | Site moisture | Soil type
1 | BMW | ++++ | Bgms
2 | BW | +++ | Bgts
3 | BMŚw | ++ | RDB
4 | BŚW | + | Bw

## Slide 20: Statistics results
Statistically significant differences in changes of soil penetration ressistance, on both depths (10 & 20 cm), p value = 0.0000
Statistically significant differences in rut depth between anaylyzed cutting areas p value = 0.0000
Moderate corelation (0.44) between rut depth and tested site

## Slide 21: Conclusions
Statistically significant differences were found in the changes of soil condensation between the examined surfaces.
Skidding trails covered an average of 28% of the studied cutting areas.
On 2.5% of the tested areas, the mineral layer of the soil was exposed as a result of passing machines.
Statistically significant differences were found in the depth of the created ruts on the examined surfaces.
There is a moderate correlation between the size of the ruts and the cutting area.

## Slide 22: Thank you for your attention
In case of any questions please contact me Dariusz.Pszenny@sggw.edu.pl