## Slide 1
Droplet formation in a cross-junction with non-Newtonian dispersed phase
Maryam Fatehifar 1,*, Alistair Revell 1, and Masoud Jabbari 1
Department of Mechanical, Aerospace and Civil Engineering, University of Manchester, Manchester, M13 9PL, UK
* Corresponding author: maryam.fatehifar@manchester.ac.uk

## Slide 2
Microfluidics enables generating series of isolated droplets for high-throughput screening. As many biological/chemical solutions are of shear thinning non-Newtonian nature [1,2], we studied non-Newtonian droplet generation to improve the reliability of simulation results in real-life assays. We considered non-Newtonian power-law behaviour for Xanthan gum aqueous solution as the dispersed phase, and Newtonian canola oil as the continuous phase. Simulations were performed in OpenFOAM, using the interFoam solver and volume of fluid (VOF) method [3].
A cross-junction geometry with each inlet and outlet channel height (H) and width (W) equal to 50 micrometer with slight contractions in the conjunctions was used to gain a better monodispersity. Following validation of the numerical setup, we conducted a series of tests to provide novel insight into this configuration.
With Capillary number (), of 0.01, dispersed phase to continuous phase flow-rate ratio of 0.05, and contact angle of 160˚, simulations revealed that by increasing the Xanthan gum concentration (0, 800, 1500, 2500 ppm) or in other words, decreasing the n -flow behaviour index- from 1 to 0.491, 0.389, and 0.302 in power-law model [4] : (a) breakup of the dispersed phase thread occurred at 0.0365, 0.0430, 0.0440, 0.0450 s; (b) the dimensionless width of the thread () at the main channel entrance increased from 0 to 0.066, 0.096, 0.16; and (c) the dimensionless droplet diameter () decreased from 0.76 to 0.72, 0.68, 0.67, respectively. Our next plan is to study effect of shear-thinning behaviour on droplet generation in different Ca and flow-rate ratios.
Abstract
Keywords: droplet microfluidics; non-Newtonian fluid; volume of fluid

## Slide 3
Traditional biomedical tests are:
being laborious
time-consuming
expensive
in need of experienced operator
Technology
Engineering
Natural Science
Biomedical Technology
prediction, diagnosis, and treatment of various inherited and acquired illnesses.
High-throughput screening (HTS) has been developed which refers to scientific experimental methods allowing rapid conduction of series of chemical and biological tests.
High-throughput Screening
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 4
Microfluidic Technology
Microfluidics is becoming a preferred choice for research and diagnosis due to two main reasons:
  low sample/ reagent consumption and high processing speed
  extreme flow confinement (Re < 1) high control over the fluid molecules in space and time
Droplet-based microfluidics
  an intriguing subject with promising future
  enables control over:
    volume
    frequency
    composition
Fig 1- Droplet microfluidics
(Taken from https://www.kth.se/pro/nanobio/droplet-microfluidics-1.366373)
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 5
Microfluidic CFD
Many researches have used CFD tools to investigate the microfluidic devices behaviour including droplet generation in different regimes and novel geometries.
Computational fluid dynamics (CFD) can investigate
  influence of different physical parameters
  their relations to generated droplets size/ frequency
  in a less expensive systematically manner.
Yet, there are some aspects in need of further investigation so that the CFD results would become more reliable and accurate.
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 6
Aim of Research
Justification:
Many biological/chemical solutions used in biotechnology
  shear thinning non-Newtonian
Most studies consider Newtonian fluids
To improve the reliability of simulation results in real-life assays
Generating series of non-Newtonian isolated droplets for high-throughput screening
Aim:
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 7
Governing Equations
Volume of Fluid (VOF) Navier-Stokes equations for both fluids is combined with advection equation for the fluid fraction α
 | (Equation 1)
 | (Equation 2)
 | (Equation 3)
 | (Equation 4)
 | (Equation 5)
 | (Equation 6)
 | (Equation 1)
 | (Equation 2)
 | (Equation 3)
 | (Equation 4)
 | (Equation 5)
 | (Equation 6)
VOF
Introduction
Methodology
Result and Discussion
Conclusion
Power-law Fluid:

## Slide 8
Software
Software:
OpenFOAM 8
  Free, open source CFD software developed primarily by OpenCFD Ltd since 2004.
Solver : interFoam
  Solver for 2 incompressible, isothermal immiscible fluids using a VOF
Multidimensional universal limiter with explicit solution (MULES) algorithm to solve the advection equation for the volume fraction
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 9
Numerical Settings
Pressure-velocity coupling: PISO scheme
Transient terms discretised scheme: first order implicit Euler
Interpolation scheme: linear
Spatial discretisation scheme: combination of second order upwind and central differencing with the van Leer limiter
Maximum Courant number: 0.5
Maximum Courant number of the interface: 0.25
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 10
Fluid Properties
Fluid | Viscosity [Pa.s] | Density [kg/m3] | n | K [Pa.sn]
water | 0.00089 | 997 | - | -
oil | 0.0223 | 930 | - | -
800 ppm (w/w) xanthan/ water | 0.076 | 997 | 0.491 | 0.0755
1500 ppm (w/w) xanthan/ water | 0.312 | 997 | 0.389 | 0.3125
2500 ppm (w/w) xanthan/ water | 0.985 | 997 | 0.302 | 0.985
Table 1- Properties of the liquids and parameters of the power-law fit of the xanthan solutions [4]
Material:
Dispersed phase: Xanthan gum aqueous solution
  non-Newtonian power-law fluid
Continuous phase: canola oil (Newtonian fluid)
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 11
Geometry
Fig 2 - Geometry of studied cross-junction
Geometry specification:
W= 50 μm
Slope of contraction/expansion = 1/5
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 12
Mesh
Fig 3 - Meshed geometry
Mesh was generated using “blockMesh”
Structured mesh
Different mesh size were studied 25 , 50, 75, 100 per 100 microns
Optimum: 50 cells per 100 microns accurate results as well as sharp interface
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 13
Validation
The results were validated against Wu et al. [6] and error was less than 7% in all studied cases.
Figure 4 - Droplet length results compared against the experimental results of Wu et al. [6] for Uo = 0.00252 (m/s) , σ = 30 (mN/m), and μo/ μw = 0.416
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 14
Results
  Droplet detachment time
  Thread width
  Droplet diameter
Increasing the Xanthan gum concentration (0, 800, 1500, 2500 [ppm])
Decreasing the n from 1 to 0.491, 0.389, and 0.302 in power-law model
In the simulations:
the capillary number and flow rate ratio were kept constant:
while the concentration of polymer and thus, the power-law index was changed.
Three effects were studied:
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 15
A. Effect on Droplet Detachment Time
Breakup of the dispersed phase thread experienced a delay by up to 23%.
Fig 5 – Effect of increasing the polymer concentration on droplet formation
Introduction
Methodology
Result and Discussion
Conclusion
Fig 6 – Effect of the polymer concentration on droplet detachment time
a
c
b
d

## Slide 16
B. Effect on Thread Width
Dimensionless width of the thread ( ) at the main channel entrance increased from 0 to 0.066, 0.096, 0.16.
Introduction
Methodology
Result and Discussion
Conclusion
Fig 7 – Effect of the polymer concentration on thread width

## Slide 17
C. Effect on Droplet Diameter
Dimensionless droplet diameter () decreased from 0.76 to 0.72, 0.68, 0.67.
Fig 8 – Effect of increasing the xanthan concentration from a) 0, b) 800, c) 1500 d) 2500 [ppm] on droplet formation
Introduction
Methodology
Result and Discussion
Conclusion
Fig 9 – Effect of the polymer concentration on droplet diameter
a
c
b
d

## Slide 18
Conclusion
Many studies that use CFD tools to investigate droplet generation, focus on Newtonian fluids only. As most of solutions used in biological tests are non-Newtonian, this gap was addressed in this research.
By considering non-Newtonian power-law fluid as dispersed phase and simulating the droplet generation using VOF in OpenFOAM 8 software , the following was achieved.
By increasing the polymer concentration:
Droplet detachment time is increased between 18% to 23%.
Necking started to occur and increased respectively.
Dimensionless droplet diameter ( ) decreased between 5.5% to 12%.
Introduction
Methodology
Result and Discussion
Conclusion

## Slide 19
Eun, Y. J., Utada, A. S., Copeland, M. F., Takeuchi, S., & Weibel, D. B. (2011). Encapsulating bacteria in agarose microparticles using microfluidics for high-throughput cell analysis and isolation. ACS chemical biology, 6(3), 260-266
Khater, A., Abdelrehim, O., Mohammadi, M., Azarmanesh, M., Janmaleki, M., Salahandish, R., ... & Sanati-Nezhad, A. (2020). Picoliter agar droplet breakup in microfluidics meets microbiology application: numerical and experimental approaches. Lab on a Chip, 20(12), 2175-2187.
Chen, Q., Li, J., Song, Y., Christopher, D. M., & Li, X. (2020). Modeling of Newtonian droplet formation in power-law non-Newtonian fluids in a flow-focusing device. Heat and Mass Transfer, 56(9), 2711-2723.
Taassob, A., Manshadi, M. K. D., Bordbar, A., & Kamali, R. (2017). Monodisperse non-Newtonian micro-droplet generation in a co-flow device. Journal of the Brazilian Society of Mechanical Sciences and Engineering, 39(6), 2013-2021.
Sontti, S. G., & Atta, A. (2019). Numerical insights on controlled droplet formation in a microfluidic flow-focusing device. Industrial & Engineering Chemistry Research, 59(9), 3702-3716.
Wu, L., Tsutahara, M., Kim, L. S., & Ha, M. (2008). Three-dimensional lattice Boltzmann simulations of droplet formation in a cross-junction microchannel. International journal of multiphase flow, 34(9), 852-864.
Soh, G. Y., Yeoh, G. H., & Timchenko, V. (2016). Improved volume-of-fluid (VOF) model for predictions of velocity fields and droplet lengths in microchannels. Flow Measurement and Instrumentation, 51, 105-115.
References

## Slide 20
Thank you for your attention
Any questions?